## Slide 1
Dataworks 2023
Systems Engineering Applications of UQ in Space Mission Formulation
April 26, 2023
Kelli McCoy, Jet Propulsion Laboratory, California Institute of Technology
Roger Ghanem, University of Southern California
© 2023 California Institute of Technology. Government sponsorship acknowledged.

## Slide 2: UQ in Systems Engineering
Systems engineering is a cross-cutting engineering function that focuses on designing, integrating, and managing complex systems over their life cycles
  The focus of this discussion is early mission formulation
Uncertainty Quantification (UQ) is the exploration of the unknown in computational and real-world applications (using probability and statistics)
How can UQ benefit Systems Engineering? Strategic systems engineering application of UQ techniques in space mission formulation can add value by:
  Stabilizing baselines
  Informing requirements
  Balancing cost and risk
UQ is necessary to capture the variability inherent in all systems and models of those systems
Domain knowledge
(engineering, physics, science)
Comp Sci (includes AI/ML, data science)
Math
UQ
Mission Architecting
V&V
Risk Management
Requirements development
Improved decision-making
© 2023 California Institute of Technology. Government sponsorship acknowledged.
Notes: Intersection bigger.

## Slide 3
e.g. particle counts/sizes from Enceladus plumes (as measured by Cassini HRD)
Boiling interface
Cryovolcanic
Informs mass collection, sample collector design, flux sensor design, trajectory selection , etc
QoIs: density, mass flux, etc…..
95%
We have some phenomenological data from a previous mission (or another ground-based source)
We have one (or more) physics models of the process (e.g. ballistic particle propagator)
We need to use the physics model to inform a science baseline, a spacecraft design, and a concept of operations, with consideration of risk and uncertainty
Space Mission Formulation Paradigm
© 2023 California Institute of Technology. Government sponsorship acknowledged.
Illustration Source: Spahn, F. 2006
Illustration Source: Southworth, B.

## Slide 4: Example: Enceladus Plume Characterization
We have a physics model (S), a ballistic particle propagator, that takes input θ and propagates ice grains to calculate a QoI, Q (e.g mass collected), along a given trajectory. We need Q=S(θ)≈D when S is provided the E7, E21 trajectories.
We wish to infer Θ, the set of unknown jet ejection characteristics at the surface, from HRD data. Θ is a joint probability distribution; we don’t know it precisely because HRD did not observe these parameters, but there is prior knowledge posed in literature.
θ= {α, dmax, dmin, dcrit, mtotal, maxexit, vgas, jet position, jet direction}
E7: 100km
E21: 50km
We have 2 flybys of Cassini HRD data, D, (particle count binned by a range of particle sizes). Because of this range, we do not know the exact particle sizes or the flux/mass HRD encountered.
To solve this parameter inference problem, we use Approximate Bayesian Computation (ABC)
QoI: quantity of interest
Once we have an updated joint distribution of θ, we can use this as input to estimate mass collected on future Enceladus trajectories and to inform instrument design
Prior distribution, pΘ(θ) formed by using published literature
The physics model is computationally expensive . Polynomial Chaos Expansion (PCE ) can aid in building a surrogate model
1
3
System Design
S: θ → Q
2
Notes: Xi, eta are rVs

## Slide 5: UQ Techniques used to Inform Engineering Analysis
ABC methods approximate the likelihood function by simulations, the outcomes of which are compared with the observed data
A candidate posterior sample, Q=S(θ), is simulated using model S, specified by a 𝜃 from the prior distribution, pΘ(θ).
If Q=S(θ) is too different from the observed data, d, the sample is rejected. The likelihood for this problem becomes:
Then we can execute Bayes Theorem.
Approximate Bayesian Computation (ABC)1
© 2023 California Institute of Technology. Government sponsorship acknowledged.
Polynomial Chaos Expansion (PCE)2
PCE is used to create a surrogate model to facilitate efficient probabilistic uncertainty analysis of the parameters of a system.
Postulate dependence of Q on subscale features, ξ , and describe this dependence in the form:
Q = Q(ξ) =
In this problem, some of the uncertainty is unique to each of the Enceladus jets (ξ) and some is common to all jets (η), resulting in 607 random variables that can now be expressed as a 13-d PCE. The equation for each jet, j=1,2,…100, becomes:
Estimate coefficients of the expansion using observations of Q=S(θ) that are experimental or numerical
  Now we can easily understand model error and compute quantities like Sobol indices
Notes: Change D-hat to S and D to d; Q to S
Data is uncertain—add this; deterministic model; comparing to random data
Distance between d-hat and D.
More dimensions, more samples; attribution (causes of uncertainty/sensitivity (mean and pdf))
Q=S; xi, eta to theta
Introduce variables/theta
What is the best way to relate eta to theta here?
Explaining inference with PCE
What kinds of scenarios would lead to having to re-estimate the PCEs?
How are different plume theories handled by this modeling?
Are beta coefficients updated with flight data, or just theta?

## Slide 6: How can we Inform Design and Mitigate Risk with this Model Infrastructure?
Pdf of mass collected over a trajectory for different collector mounting positions
© 2023 California Institute of Technology. Government sponsorship acknowledged.
Do small particle sizes clog insitu instruments?
Do large particles pose safety issue for mission?
Derive input parameter linear and nonlinear relationships, given Cassini data
What collector size and collector efficiency is needed to ensure high sample collection margin, subject to cost, mass, constraints?
Pdf of Mass flow rate by particle size bin
Pdf of Mass Collected over a trajectory for given collector sizes
Can the mission instrument suite accept this mass flow rate for certain particle sizes or will there be dead time?
Parameter inference
Model input parameter nxn comparison
Where on the spacecraft should the collector be mounted to maximize mass collected?
More avg mass collected with larger aperture but this may violate other system constraints
More avg mass collected with nadir positioning

## Slide 7: Using PCE to support trajectory design
Can we learn how to fly optimally to collect the most sample and ensure we meet science objectives? Where should we fly? How low? Target a jet? These decisions all have system design implications…
Flux contributed
We can construct a surrogate PCE that closely replicates each flyby and is computationally faster to work with and update with new knowledge (possibly inflight)
We can use the PCE to learn contributions from each jet on each flyby and make trajectory recommendations regarding jets to target in flight and at what angle
Mass collected on given trajectory (20 flybys)
Low altitude jet-targeted flybys (14, 16, 18, 20) get slightly more mass, but does it warrant a sophisticated attitude control system?

## Slide 8: Summary
Leveraging Uncertainty Quantification for Systems Engineering analysis and design decisions is critical (especially for highly uncertain planetary environments)
  Without UQ, we do not acknowledge or understand the breadth of risk and therefore it is difficult make informed design decisions
MMOD/Orbital debris
Reliability
Trajectory optimization
Manufacturing/materials
Autonomy, Controls
V&V/test planning
Technical resource management
Project Protection/cybersecurity
Risk Management
Requirement development
Margin assessments
Examples of systems engineering areas where UQ techniques are a logical companion:
© 2023 California Institute of Technology. Government sponsorship acknowledged.

## Slide 9: References
1. Sunnaker et al. Approximate Bayesian Computation. Computational Biology, 2013.
2. Soize, Christian; Ghanem, Roger. "Physical Systems with Random Uncertainties: Chaos Representations with Arbitrary Probability Measure. SIAM Journal on Scientific Computing. 26 (2): 395–410, 2004
© 2023 California Institute of Technology. Government sponsorship acknowledged.