## Slide 1: DATAWorks 2024 Development, Test, and Evaluation of Small-Scale Artificial Intelligence (AI)
Dr. David Bauer
MAJ David Niblick
Dr. Daniel Owens
Notes: 5 min intro, context, goals – David N
  Mission of AI team at ATEC
  Real world purpose for model; also great “test case” for methodologies
  What is AI, really? For TE, consider black box, data centric, “new”, user trust
5 min data explanation – David B
5 min model explanation – David B
5 min TE approach explanation – David N
  Identify needs/conditions of user and system, limitations of test data amount, external affect -> sensitivity analysis w/ aug data (wind, event clustering, height, type of event); must explain risk associated with each
5 min results – David N
5 min themes, lessons learned – David N
  AI includes much more not covered here (ethics, traceability, dynamic learning, etc)
  When limited in TE capabilities (unavoidable in AI/ML), must focus on managing risk
  “Test loop” must be as “easy” as possible while being thorough -> starts in system requirements (be in DevSecOps loop)
  Deep understanding of data (and flaws) is critical for both sides

## Slide 2: Agenda
Purpose
Dataset
Solution
Test and Evaluation Approach
Results
Observations and Lessons Learned

## Slide 3: Purpose
Mission of ATEC, AI Team
Small scale model could solve real-world problems at ATEC while serving as “test case”
What is AI in the context of Test and Evaluation?
Notes: AI considerations:
Novel Techniques
Understandability and Predictability
Data centric
Safety / Operational / Ethical Risk – low risk, so good test case
User Interaction with AI component

## Slide 4: Dataset
Acoustic trilateration using real data from 12 sensor array
Each sensor identifies events; time differences between sensors used to calculate location
Event detection nontrivial – lends itself to AI solution
Note: Blue lines depict acoustic signals across 12 sensors. Red dashes depict manually-determined event labels.
Example Triangulation Data
Time
Acoustic Magnitude

## Slide 5: Problem Complexity
Imperfect, inconsistent “labels” for training and testing
Lack location “ground truth”; only hand-labeled impact times
Matching order of events across sensors significantly affects location calculation
Limited amount of data
Different types of events and sensors complicate process
Sample of labeled data from single test containing multiple sensors (rows) and events (columns). Labels are depicted with red lines. Discrepancies in the labeled data are highlighted with red boxes.
Notes: Imperfect “labels” – YPG engineers selected labels that were good enough for their tests, but suffered inconsistencies; very few “ground truths” based on location
Lacked location “ground truth” – only hand-labeled impact times
Matching order of impacts across sensors – due to temporal proximity of some impacts, the order at which their sound “hits” the sensors might be mixed; this creates significant error in triangulation calculations
Limited amount of data
Different types of sensors shape different “signatures” in acoustic measurements

## Slide 6: Evolution of Detection Algorithm
DNN
64-sample blocks
Looks for event in middle of block only
DNN
512-sample blocks
Returns a set of probabilities and positions of potential events
Hybrid
Uses a spectrogram to find rough area of potential events
Uses medium block DNN to scan areas found by spectrogram
Peaks
Filtering + Peaks
Uses a purely time-domain peak-finder library
Uses a series of filters and peak-finding steps
Combines results from two parallel algorithms
Genetic ML
Used (evolutionary) genetic algorithm to find optimal parameters for the filtering + peak detection algorithm.
Very slow!
Slow!
Fast
Fast
Fast
Accuracy issues with close and complex events
Improving accuracy
Fast
Notes: ** Why? What drove changes?
Notes:
Didn’t continue short-block DNN development long enough to compare with later methods.
Medium block DNN accuracy improved over time, especially when labeling

## Slide 7: Evolution of Event Location Estimation Algorithm
Matching Detections
Position Estimation
Direct Generation
Simulated Annealing
Masking
Heuristics
Single Path
Many Candidates
Expanded Searches
Recursive Grid Search
Direct Position Generation
Weather Compensation
Integer programming problem (hard). Does not handle detection misses and false positives well.
Continuous optimization problem (easier). Natural handling of detection misses.
Faster methods for generating event location candidates.

## Slide 8: Test and Evaluation Approach
Data
Plan
Execute
Evaluate
Refine
Environment
Conditions
Requirements
Capabilities
Limitations
Risks
Notes: Opportunity for us to practice our T&E method in “sandbox” fashion
Identify
  needs/conditions of user and system,
  limitations of test data amount,
  external affects on system
Does plan change if model is “AI”?
sensitivity analysis w/ augment data (wind, event clustering, height, type of event);
Must explain risk associated with conditions – test can’t cover it all
  For example, if system needs to triangulate new type of “event’, needs portable T&E to validate
Must be as rapid/automated as possible – users ideally

## Slide 9: Results
Location Error
Average: 121 m
Median: 10.5 m
Model produces mix of acceptable results and extreme outliers
Location Error Histogram
+

## Slide 10: Results
Event Spread and Atmospheric Conditions have little impact on accuracy
Location Error vs Event Spread
Atmospheric Effect on Error
Pearson P-Value: 0.23
Pearson P-Value: 0.78

## Slide 11: Results
Error By Elevation Type |  | 
Metric | Air | Ground
Location Error (Mean, m) | 314 | 8.15
Location Error (Median, m) | 285 | 3.91
Model fails at air events!
Box Plot Comparing Air to Ground Events
T-Test P-Value: 1.15e-16

## Slide 12: Results
Error (Ground) By Event Type |  | 
Metric | Type X | Type Y
Location Error (Mean, m) | 3.11 | 8.87
Location Error (Median, m) | 2.29 | 4.01
Possible increased risk with Type Y,
but both meet standard.
Box Plot Comparing Type X and Type Y Events (Ground Only)
T-Test P-Value: 0.28

## Slide 13: Evaluation
System meets requirements (under certain conditions)
Event clustering and atmospheric conditions have little effect on error
Current model not usable with air events
Possible increased risk for Event Type Y; Need to validate with every new event type

## Slide 14: Observations
Data understanding central to both development and T&E
Manage risk through lens of environment and conditions – communicate through capabilities and limitations
“Test loop” must be as automated as possible
  Starts in system requirements
  Ideally user can validate on location after deployment
Notes: T&E of AI includes much more not covered here (ethics, traceability, dynamic learning, etc)… each one of those could be an entire symposium