## Slide 1: Introduction to Uncertainty Quantification for Modeling and Simulation
Jim Warner
NASA Langley Research Center
Hampton, VA
DATAWorks 2023 – Mini Tutorial 6
Alexandria, VA
April 27th, 2022

## Slide 2: What is Uncertainty Quantification (UQ)?
  So how wrong might our models be?
  (When) are they useful from an engineering perspective?
  And how confident are we in their predictions?
UQ provides a framework for answering these questions and making our models useful.
“All models are wrong,
George E.P. Box
but some are useful”
Real world
Model
Model + UQ
Models Vs. Reality
Scenario 1
Scenario 2
Quantity of Interest

## Slide 3: What is Uncertainty Quantification (UQ)?
Probability & Statistics
Computing
Engineering
UQ
“…the science of identifying, quantifying, and reducing uncertainties associated with models, numerical algorithms, experiments, and predicted outcomes…” Smith, R. C. Uncertainty Quantification Theory, Implementation, and Applications. 2013.
Imbue our models with what we know, what we don’t know, and to what degree we don’t know it in order to get a more complete picture of what we’re modeling.

## Slide 4: Experiments, Models, Simulations, and UQ
Uncertainty quantification (UQ): the quantification of the effect of various sources of error (from model, simulation, experiment) on a predicted quantity of interest
Model verification: the process of quantifying the accuracy of simulation codes used to implement mathematical models (i.e. are we solving the equations correctly?)
Model validation: the process of determining the accuracy with which mathematical models represent the physical processes of interest (i.e. are we solving the correct equations?)
Model Verification
Model calibration and validation
Model Formulation
Physical Experiment
Numerical Simulation
Mathematical Model
Input parameter uncertainty
Discretization error
Sensor error
Example sources of uncertainty
Quantity of interest
Prediction
Probabilistic
Smith, R. C. Uncertainty Quantification Theory, Implementation, and Applications. 2013.
Probability Density
Quantity of interest
Notes: From here on – “model” and “simulation” will be synonomous

## Slide 5: Computational Models: Notation and Examples
Model
Inputs
Outputs
Max contact force
Atmosphere conditions
Mass properties
Landing location
Impact velocity
Material properties
Spacesuit Impact Model
Trajectory Simulation
Transonic Aero Solver
Wing geometry
Mach number
Lift
Ocean temps.
Initial pressures wind speeds
Storm path
Weather Model
Disease Dynamics Model
Infection rate
Birth rate
Death rate
Total infected
S
I
R
Often distinguish between inputs and parameters
Often distinguish between outputs and quantities of interests (QoIs)
Notes: EDL – D205
Aero – D308

## Slide 6: Today’s Goals and Points of Emphasis
Provide enough information to know what to ask/search for if interested in applying UQ
  Broad overview of the main concepts; listing common references, software, methods for further study
  Understand “what/why/when", not necessarily “how”
Provide parallels, results from practical NASA problems

## Slide 7: Quick Review of Terminology
Random Variable,
  Variable with unknown true value
Probability Density Function (PDF),
  Function describing the relative likelihood that takes a specific value,
Cumulative Distribution Function (CDF),
  Probability that takes a value less than or equal to
  CDF = integral of the PDF from to
  Can obtain other probabilities by integrating the PDF; e.g.,
a
b
PDF
a
b
1
0
CDF
More likely
Less Likely

## Slide 8: UQ Concepts
(Computational)

## Slide 9: UQ Concepts

## Slide 10: UQ Concepts: Uncertainty Propagation
  Uncertainty propagation feeds quantified input uncertainties through our model to produce probabilistic predictions
Uncertainty Propagation

## Slide 11: Uncertainty Propagation
Computational Model
Input Parameters
Quantity of Interest (QoI)
e.g.,
Loads/forces
Atmosphere conditions
Infection rates
e.g.,
Max. impact stress
Landing location
Total # infected
e.g.,
Spacesuit impact
Trajectory simulation
Disease dynamics
Given PDFs for uncertain input parameters, , and a governing computational model, , of a system/structure, estimate the _______ of/for the QoI:
  PDF:
  Expected value (i.e., the mean), standard deviation of the QoI:
  95% credible intervals: such that
  Probability of exceeding a critical value:

## Slide 12: Uncertainty Propagation
Computational Model
Input Parameters
Quantity of Interest (QoI)
Given PDFs for uncertain input parameters, , and a governing computational model, , of a system/structure, estimate the _______ of/for the QoI:
  PDF:
  Expected value (i.e., the mean), standard deviation of the QoI:
  95% credible intervals: such that
  Probability of exceeding a critical value:

## Slide 13: Uncertainty Propagation
Computational Model
Input Parameters
Quantity of Interest (QoI)
Given PDFs for uncertain input parameters, , and a governing computational model, , of a system/structure, estimate the _______ of/for the QoI:
  PDF:
  Expected value (i.e., the mean), standard deviation of the QoI:
  95% credible intervals: such that
  Probability of exceeding a critical value:

## Slide 14: Uncertainty Propagation
Computational Model
Input Parameters
Quantity of Interest (QoI)
Given PDFs for uncertain input parameters, , and a governing computational model, , of a system/structure, estimate the _______ of/for the QoI:
  PDF:
  Expected value (i.e., the mean), standard deviation of the QoI:
  95% credible intervals: such that
  Probability of exceeding a critical value:

## Slide 15: Uncertainty Propagation
Computational Model
Input Parameters
Quantity of Interest (QoI)
Given PDFs for uncertain input parameters, , and a governing computational model, , of a system/structure, estimate the _______ of/for the QoI:
  PDF:
  Expected value (i.e., the mean), standard deviation of the QoI:
  95% credible intervals: such that
  Probability of exceeding a critical value:

## Slide 16: Monte Carlo (MC) Simulation
Computational Model
Input Parameters
Quantity of Interest (QoI)
Procedure – repeat following times:
  Generate random sample of input parameters:
  Evaluate model & store output:
Then – postprocess output samples to estimate PDF, statistics of QoI, etc.
  (use histogram or kernel density estimate)
  (expected value sample average)
  (failure probability proportion of samples that failed)
Indicator function: = 1 if True, = 0 if False

## Slide 17: MC Example: Beam with Random Loading
Computational Model
Input Parameters
Uncertain load parameters (F, W)
Fixed, deterministic inputs:
  Length (L), stiffness, area

## Slide 18: MC Example: Beam with Random Loading
Input Parameters
Computational Model
Quantity of Interest (QoI)
0.550
Model predictions for three randomly drawn inputs
Uncertain load parameters (F, W)
Fixed, deterministic inputs:
  Length (L), stiffness, area

## Slide 19: MC Example: Beam with Random Loading
Computational Model
Failure threshold
Monte Carlo simulation for N=10,000 random samples
Input Parameters
Quantity of Interest (QoI)
in
Uncertain load parameters (F, W)
Fixed, deterministic inputs:
  Length (L), stiffness, area

## Slide 20: Example: Beam with Random Loading
#Specify inputs
...
#Monte Carlo simulation loop:
deflection_samples = np.zeros(N)
for i in range(N):
F = random.normal(F_mean, F_std)
W = random.normal(W_mean, W_std)
deflection_samples[i] = F*L**3/(48.*E*I)+(5*W*L**4)/(384.*E*I)
#Postprocess to create histogram, estimate statistics:
plt.hist(deflection_samples)
mean = numpy.mean(deflection_samples)
failure_prob = numpy.sum(deflection_samples>=failure_threshold)/N
Monte Carlo implementation (e.g., Python):
Draw random input samples
Evaluate model
Set N, L, F_mean, F_std, …
Uncertain load parameters (F, W)
Fixed, deterministic inputs:
  Length (L), stiffness, area

## Slide 21: MC: Convergence
Convergence rate is on order of (via Central Limit Theorem) and is independent of input dimension
Rare event (e.g., probability of failure) estimators require significantly more samples for accuracy
Notes: Mention Central Limit Theorem implication: As the number of input samples, regardless of their type of distributions, the expected value of output of the model is going to asymptotically approach a Gaussian or normal distribution.
Also note: convergence rate is on the order of 1/sqrt(N) regardless of input PDF as well, but input PDF would affect the constant of proportionality.

## Slide 22: MC: Effect of Correlated Inputs
Uncorrelated
Marginal PDFs of loads
Joint PDF of loads
Monte Carlo simulation
No correlation:
Correlation = 0
Failure Threshold

## Slide 23: MC: Effect of Correlated Inputs
Joint PDF of loads
Correlation = 0
Correlation = 0.95
Uncorrelated
Marginal PDFs of loads
Correlated
Monte Carlo simulation
No correlation:
Failure Threshold

## Slide 24: MC: Effect of Correlated Inputs
Correlated load case is over 4X more likely to fail
No correlation:
With correlation:
Joint PDF of loads
Correlation = 0
Correlation = 0.95
Uncorrelated
Marginal PDFs of loads
Correlated
Loads more likely to take extreme values together
MC simulation
Important to quantify correlations; failure to do so can lead to undetected non-conservatism
Failure Threshold

## Slide 25: MC Takeaways
  Non-intrusive, general-purpose, and relatively simple approach for propagating uncertainty through models
    But can be challenging/infeasible in practice when models are expensive
  Exhibits provable convergence at a known rate, regardless of input dimension
  Improperly specifying input uncertainty (e.g., parameter correlations) can have a significant impact on results
So how do we quantify input uncertainties?
Make estimates based on expert judgement
Use available data to infer uncertainty directly

## Slide 26: UQ Concepts: Model Calibration
Model Calibration
  Model calibration explicitly quantifies model input uncertainties using experimental data (can be used to improve or update initial assumptions)

## Slide 27: Model Calibration with Component Scale Tests
In practice, the experimental data available for calibration is often from a simpler, component scale test
Examples from spacesuit reliability analyses:
Brief
Soil
Rock
Model Calibration
Low Velocity Impact Test
Force vs Time Data
Composite Coupon Impact Model
Model Calibration
Rover with Cone Penetrometer
Lunar Regolith Resistance Data
Penetrometer Model
Progressive damage model parameters
Mohr Column soil model parameters
Modeling Progressive Impact Damage in Composites
Modeling Suit Impact on Lunar Regolith

## Slide 28: Deterministic vs. Probabilistic Calibration
Assume:
  is measurement data from experiment, , with measurement error/noise,
  is a computational model that predicts the measured quantity from the experiment
Deterministic calibration:
  Find deterministic parameters that result in best agreement by minimizing some error metric; e.g., sum of squared error,
Probabilistic calibration:
  Find a PDF, , assigning probability density to all potential values of the parameters based on the observed data and accounting for noise
Y
Y

## Slide 29: Probabilistic Calibration
Formulated such that is high when error, , is low and vice versa
  Typically implemented using Bayesian inference
  Starts with an initial guess for uncertainty (“prior distribution”) then updates it using the measurement data (with a “likelihood function”)
Prior
Likelihood
Posterior
x
Probability
Weak/non-informative prior
x
Probability
Strong prior
“Find a PDF, , assigning probability density to all potential values of the parameters based on the observed data and accounting for noise ”
How does this work in practice?

## Slide 30: Probabilistic Calibration Takeaways
Estimates input uncertainties based on data, accounting for noise
The calibrated PDF naturally includes estimates of correlations and noise level
Less data  more uncertainty; more data  less uncertainty
Variety of well-established methods exist for performing probabilistic calibration
Some notable caveats:
  Requires specific expertise/experience
  Prior distribution specification more nuanced than you may expect
  Computationally expensive relative to deterministic calibration

## Slide 31: UQ Concepts: Surrogate Modeling (AKA response surfaces, reduced order models, …)
Machine Learning
Gaussian processes
Neural networks
Polynomial Chaos
….
High-Fidelity
Simulation
Input
Training Data
Output
Training Data
…
Surrogate
Model
Offline
Online
  Overcoming computational burden when the model is expensive
…
Orders of magnitude computational speedup possible
Notes: Aka reduced order modeling aka response surface aka

## Slide 32: Surrogate Model Validation
Regardless of the method used for surrogate modeling, the most important step is validating a trained model before using for UQ
Always create a separate dataset for testing that is not used for training
If surrogate model error is not negligible, it can be factored into total uncertainty when making probabilistic predictions
…
…
…
…
Training
Testing
(M < T)
Compare predictions on test data to the original model

## Slide 33: UQ Concepts: Model Discrepancy
“All models are wrong,” but our objective is to make them useful
  Physics never perfectly represented  capture the important parts!
In some cases, missing physics can lead to significant model discrepancy
  Significant meaning model form errors are on the same order as other sources of uncertainty
  Can often be identified as a violation of assumptions about the noise in the measurements during calibration
  Often results from a model not matching the as-built system
Y
Linear Model
“True” nonlinear function
Notes: Mismatch from as built system ex: stiffening members with incorrect dimensions and/or in the wrong locations

## Slide 34: UQ Concepts: Model Discrepancy
“All models are wrong,” but our objective is to make them useful
  Physics never perfectly represented  capture the important parts!
In some cases, missing physics can lead to significant model discrepancy
  Significant meaning model form errors are on the same order as other sources of uncertainty
  Can often be identified as a violation of assumptions about the noise in the measurements during calibration
Potential consequences:
  Biased estimates of physical parameters
  Invalidated inverse problem formulation
  Inaccurate estimates of uncertainty, especially when extrapolating

## Slide 35: UQ Concepts: Model Discrepancy
“All models are wrong,” but our objective is to make them useful
  Physics never perfectly represented  capture the important parts!
In some cases, missing physics can lead to significant model discrepancy
  Significant meaning model form errors are on the same order as other sources of uncertainty
  Can often be identified as a violation of assumptions about the noise in the measurements during calibration
Remedies:
  Implement an advanced calibration method to attempt to learn the discrepancy
  Build a better model (using insights from UQ analysis); Ensure the model matches the as-built hardware as close as possible
Potential consequences:
  Biased estimates of physical parameters
  Invalidated inverse problem formulation
  Inaccurate estimates of uncertainty, especially when extrapolating

## Slide 36: UQ Concepts: Sensitivity Analysis
Sensitivity Analysis
  Sensitivity analysis identifies the most influential system parameters to properly focus effort/resources in a probabilistic analysis

## Slide 37: Sensitivity Analysis Overview
Local sensitivity analysis – based on derivatives,
  Computationally efficient
  Does not consider input uncertainty, model non-linearity
Global sensitivity analysis
  More computationally expensive
  Holistically assesses effect of uncertainty & model behavior
  Used to reduce dimensionality or inform additional experiments
*Global sensitivity analysis. The primer. Andrea Saltelli. 2007.
Local sensitivity at x* is small
x*
Xi
Y
Sensitivity
Input 4
Input 3
Input 1
Input 2
How uncertainty in the output of a model can be apportioned to different sources of uncertainty in the model input*

## Slide 38: Practical Example – Spacesuit Reliability
Note: this example is presented for purposes of demonstration; the reliability estimates provided here are not reflective of the true values for these projects
Estimating the reliability of a spacesuit for impact events (e.g., astronaut falls on the lunar surface) using UQ
Probability of fall
Probability of impact location
Mission-related probabilities
Impact velocity uncertainty
Material Uncertainties
Probability of rock size
Impact Damage Simulation
Variability in lunar regolith

## Slide 39: Z-2 Spacesuit Reliability Analysis
Sensitivity Analysis
Component Model
Z-2 Design
Impact Model
Output
Max. Impact Force
Inputs
Impact Load
Material Model
Material Parameters
Impact Velocity
Probability of failure
Failure Threshold
Reliability
Uncertainty Propagation
Model Calibration
Impact Test Data
Sensitivities
UQ Workflow Applied to Z-2 Spacesuit Reliability
Notes: Point out

## Slide 40: Z-2 Spacesuit Reliability Analysis
Sensitivity Analysis
Component Model
Z-2 Design
Impact Model
Output
Max. Impact Force
Inputs
Impact Load
Material Model
Material Parameters
Impact Velocity
Given: candidate design, component/impact models, test data, assumed impact load & failure criteria
Estimate: Z-2 impact reliability
Probability of failure
Failure Threshold
Reliability
Uncertainty Propagation
Model Calibration
Impact Test Data
Sensitivities
UQ Workflow Applied to Z-2 Spacesuit Reliability
Z-2 fails if:
Max. impact force > 2800lbf
Notes: Point out

## Slide 41: Z-2 Spacesuit Reliability Analysis
Sensitivity Analysis
Component Model
Z-2 Design
Impact Model
Output
Max. Impact Force
Inputs
Impact Load
Material Model
Material Parameters
Impact Velocity
Given: candidate design, component/impact models, test data, assumed impact load & failure criteria
Estimate: Z-2 impact reliability
Probability of failure
Failure Threshold
Reliability
Uncertainty Propagation
Model Calibration
Impact Test Data
Sensitivities
UQ Workflow Applied to Z-2 Spacesuit Reliability
Notes: Point out

## Slide 42: Z-2 Spacesuit Reliability Analysis
Sensitivity Analysis
Component Model
Z-2 Design
Impact Model
Output
Max. Impact Force
Inputs
Impact Load
Material Model
Material Parameters
Impact Velocity
Given: candidate design, component/impact models, test data, assumed impact load & failure criteria
Estimate: Z-2 impact reliability
Probability of failure
Failure Threshold
Reliability
Uncertainty Propagation
Model Calibration
Impact Test Data
Sensitivities
UQ Workflow Applied to Z-2 Spacesuit Reliability
  1) Applied sensitivity analysis to identify the most influential material model parameters to focus on for the remaining UQ analysis
Notes: Point out

## Slide 43: Z-2 Spacesuit Reliability Analysis
Sensitivity Analysis
Component Model
Z-2 Design
Impact Model
Output
Max. Impact Force
Inputs
Impact Load
Material Model
Material Parameters
Impact Velocity
Given: candidate design, component/impact models, test data, assumed impact load & failure criteria
Estimate: Z-2 impact reliability
Probability of failure
Failure Threshold
Reliability
Uncertainty Propagation
Model Calibration
Impact Test Data
Sensitivities
UQ Workflow Applied to Z-2 Spacesuit Reliability
  2) Used model calibration to quantify uncertainty in material parameters from impact test data
Notes: Point out

## Slide 44: Z-2 Spacesuit Reliability Analysis
Sensitivity Analysis
Component Model
Z-2 Design
Impact Model
Output
Max. Impact Force
Inputs
Impact Load
Material Model
Material Parameters
Impact Velocity
Given: candidate design, component/impact models, test data, assumed impact load & failure criteria
Estimate: Z-2 impact reliability
Probability of failure
Failure Threshold
Reliability
Uncertainty Propagation
Model Calibration
Impact Test Data
Sensitivities
UQ Workflow Applied to Z-2 Spacesuit Reliability
  3) Used uncertainty propagation to estimate reliability given material/impact load uncertainty
    Reliability 99.3% (demonstration purposes only)
    Quantified material uncertainty resulted in >10% variability in predicted max. contact force
Notes: Point out

## Slide 45
Lunar regolith properties
Model Calibration – Lunar Regolith Uncertainty
Rover with Cone Penetrometer
Lunar Regolith Resistance Data*
*Heiken, Grant H., David T. Vaniman, and Bevan M. French. Lunar Sourcebook, a user's guide to the Moon. 1991.
Probabilistic ​
Model
Calibration
Depth
Force
Shear Modulus
Poisson Ratio
Friction Angle
Cohesion
Cohesion Gradient
Shear Modulus
Poisson Ratio
Friction Angle
Cohesion
Cohesion Grad.
Density
Soil Model Parameters
Force
Depth
Penetrometer Model
Soil
Cone Penetrometer

## Slide 46: Summary
Uncertainty Quantification provides a framework to quantify what we know, what we don’t know, and to what degree we don’t know it, in the context of modeling & simulation
  Monte Carlo simulation is a general-purpose, simple-to-implement method for uncertainty propagation, but:
  It can be difficult to know which input parameters should be treated as random variables
    Potential solution: sensitivity analysis
  It can be difficult to properly assign probability distributions to input parameters
    Potential solution: model calibration
  It can be intractable for expensive, high-fidelity models
    Potential solution: surrogate modeling

## Slide 47: Summary - Common UQ Pitfalls
Using solutions that are not converged (e.g., not enough samples for Monte Carlo)
Assuming all input parameters are independent/uncorrelated to simplify an analysis
Failing to validate a surrogate model (or validating using the same data it was trained on)
Not accounting for significant model discrepancy / model form uncertainty

## Slide 48: Further Reading
Uncertainty Quantification (general)
  Smith, R. C. Uncertainty Quantification Theory, Implementation, and Applications. 2013. [Textbook]
  Roy, C. J. and Oberkampf, W. L. A comprehensive framework for verification, validation, and uncertainty quantification in scientific computing. 2010.
  Warner, J. E. et al.: “Assessing Next-Gen Spacesuit Reliability: A Probabilistic Analysis Case Study”, NASA/TM–20210019495. 2021.
Uncertainty Propagation
  Rubinstein, R. Y. and Kroese, D. P. Simulation and the Monte Carlo Method., 2016.
  Ditlevsen, O. and Madsen, H. O. Structural Reliability Methods. 2007. [Textbook] (Free PDF download available)
Model Calibration
  Kennedy, M. C. and O’Hagan, A. Bayesian calibration of computer models. 2002.
  Haugh, M. B., A Tutorial on Markov Chain Monte-Carlo and Bayesian Modeling. 2021.
Surrogate Modeling
  Alizadeh, R. et al. Managing computational complexity using surrogate models: a critical review. 2020.
  Gramacy, R. B. Surrogates: Gaussian Process Modeling, Design and Optimization for the Applied Sciences. 2020.
  Sudret, B. et al. Surrogate models for uncertainty quantification: An overview. 2017.
Model Discrepancy
  Brynjarsdóttir, J. and O’Hagan, A. Learning about physical parameters: The importance of model discrepancy. 2014.
  Soize, C. A nonparametric model of random uncertainties for reduced matrix models in structural dynamics. 2000.
Sensitivity Analysis
  Saltelli, A. Global sensitivity analysis. The primer. [Textbook] (Free PDF download available)
  Plischke, E. et al. Global sensitivity measures from data. 2013.
Software
  Dakota: uncertainty quantification software by Sandia: https://dakota.sandia.gov/
  SALib: open-source Python library for sensitivity analysis https://github.com/SALib/SALib
  Scikit-learn: open-source Python library for machine learning (surrogate modeling): https://scikit-learn.org/stable/
Email: james.e.warner@nasa.gov

## Slide 49
Backup

## Slide 50: Philosophical Points
Types of uncertainty:
  Aleatory uncertainty – uncertainty due to inherent variability or randomness of a physical phenomenon
    E.g., Variability of material properties in manufactured parts; variation in environmental load
  Epistemic uncertainty – uncertainty due to a fundamental lack of knowledge or simplifying model assumptions, missing physics, measurement bias, etc. that could theoretically be reduced with additional resources/effort
    Ex: the geometry of a specific manufactured part; numerical error from a coarse mesh
Two schools of thought:
  Bayesian: probability represents degree of belief of the analyst and can be used to model both aleatory & epistemic uncertainties
  Frequentist: probability represents the frequency of occurrence and therefore is not appropriate for epistemic uncertainties; instead intervals with no associated likelihood/PDF should be used.
“The Bayesian perspective is… natural for model uncertainty quantification since it provides densities that can be propagated through models.” Smith, R. C. Uncertainty Quantification Theory, Implementation, and Applications. 2013.

## Slide 51: Model Discrepancy Details
Model validation / model discrepancy / model form uncertainty
  One approach: calculate validation error metric at series of points in validation domain & build regressor to estimate model form uncertainty in application domain [1]
References
  Roy, C. J. and Oberkampf, W. L. A comprehensive framework for verification, validation, and uncertainty quantification in scientific computing. 2010.
    Model-form uncertainty estimation + extrapolation (images above)
  Kennedy, M. C. and O’Hagan, A. Bayesian calibration of computer models. 2002.
    Bayesian approach to treating model discrepancy
  Sills, J. NESC-RP-16-01110, NASA/TM-2021-0009733. 2021.
    Non-parametric variation approach for model form uncertainty for dynamics
Validation metric based on experiment/simulation CDFs [1]
Validation vs. Application Domains [1]

## Slide 52: Important Areas Not Covered
Mixed and Imprecise Probability Methods
  Philosophy: aleatory (irreducible/stochastic) uncertainty is modeled with probability distributions, epistemic (reducible/ignorance) uncertainty is modeled with intervals with no associated probability
  Solution approach: double loop Monte Carlo simulation
    Repeat: select possible epistemic variable values from intervals, perform standard Monte Carlo simulation for aleatory variables; Then: identify min/max CDFs to create P-Box solution
  Provides estimates in the form of intervals:
    P(y < 5) = [0.2, 0.7]; Probability of failure = [0.97, 0.9999]
  Simple, efficient compromise: use worst case values for epistemic variables & use standard Monte Carlo
    Can be challenging to identify “worst case” values for large numbers of epistemic uncertainties and complex failure criteria
References
  Roy, C. J. and Oberkampf, W. L. A comprehensive framework for verification, validation, and uncertainty quantification in scientific computing. 2010.
  Ferson, S. and Ginzburg, L. R. Different methods are needed to propagate ignorance and variability. 1996
Computational Model
Input Parameters
Quantity of Interest (QoI)
Aleatory
Epistemic
CDF
P-Box
Width reflects level of ignorance

## Slide 53: Factor of Safety- vs. Reliability-Based Design
Images adapted from Raju et al. White Paper on Factors of Safety. NASA/TM-2009-215723
Factor of Safety
Knockdown factor
Load
Resistance
Margin
Calculated
Calculated
Traditional Design Based on FoS
Probability Density
Load or Resistance
Load
Resistance
Failure Probability
Reliability-Based Design
FoS Shortcomings
  Determined empirically, not necessarily based on physics/mathematics
    Inconsistencies observed from program to program; between NASA and other external organizations
    Difficult to specify for new vehicle types, materials, and environments
  May be sequentially applied by multiple teams
    Can be costly, conservative, inefficient
  Does not provide measures of reliability from the design process

## Slide 54: Factor of Safety- vs. Reliability-Based Design
Images adapted from Raju et al. White Paper on Factors of Safety. NASA/TM-2009-215723
Factor of Safety
Knockdown factor
Load
Resistance
Margin
Calculated
Calculated
Traditional Design Based on FoS
Probability Density
Load or Resistance
Load
Resistance
Failure Probability
Reliability-Based Design
Reliability-Based Design
  Classical structural reliability assumes load & resistance are independent, Gaussian distributions and yields a simple analytical formula for probability of failure
  The resistance (strength) distribution can be determined directly from A/B-basis properties
  For practical problems, more general UQ methods are often needed to estimate the load (stress) distribution or the probability of failure (P[L > R]) directly – the focus of today’s slides

## Slide 55: SimTools: In-House Software for Automating Simulations
Example: Needed to run 200 suit simulations for different inputs; Ran 15 simulations at a time on 10 processors each
  Performed 1+ years of serial computation time in around 1 week of wall time
Inputs
Outputs
High Performance Computing Cluster Scheduling
Postprocessing & Data Management
Specify:
Number of input samples/combinations
Number of simulations to run in parallel
Number of processors to run each simulation on
Output metrics to compute & store
Produces:
Processed input/output dataset
AM1 | … | VEL
12.4 | … | 1.0
14.3 | … | 1.4
… | … | …
13.1 | … | 1.1
x | y | x | k | d | e | 3
1 | 2 | 3 | 5 | 2 | 5 | 3
3 | 3 | 3 | 2 | 2 | 2 | 3
3 | 2 | 2 | 2 | 2 | 2 | 2
0 | 9 | 8 | 6 | 5 | 4 | 3
F-max | E-Max
1.2 x 103 | 5.4 x 103
1.8 x 103 | 4.9 x 103
… | …
1.6 x 103 | 5.8 x 103
1
2
3
…
4
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
Nominal FEM model
Param1
Prob
Param2
Prob
Prob
Param3
Impact Velocity
Prob
Input Distributions or bounds
Outputs
Inputs