## Slide 1: Active Learning with Bayesian Optimization: A Modern Framework for Faster Testing
DATAWorks 2026
Institute for Defense Analyses
Alexandria, VA
Tom Donnelly, Systems Engineer
tom.donnelly@jmp.com
Chris Gotwalt, Chief Data Scientist
christopher.gotwalt@jmp.com

## Slide 2: Outline
Bayesian Optimization overview
    What it is
    How it works
    Where is it useful
    Potential gotchas
Open-Source Tools
Basic Bayesian Optimization
  How the Max Expected Improvement acquisition function works
Examples
    Finding one of multiple optima for a complex deterministic process
    Rescuing an OFAT experiment and optimizing three responses
Exotic Bayesian Optimization
Benefits/Value

## Slide 3: Bayesian Optimization Overview
What is Bayesian Optimization:
Iterative optimization algorithm – an active learning approach – for quickly finding the best combination of factor settings to satisfy your response goals
Method for finding the max or min of functions that are expensive to evaluate, by intelligently choosing the next point to sample based on past results.
Generative learning technique that often uses a Gaussian Stochastic Process (GaSP) model as a base to generate new candidate runs.

## Slide 4: Bayesian Optimization Overview
How does Bayesian Optimization work:
Start with some existing data (historical data or designed experiment).
Construct initial GaSP model to approximate unknown function.
Use an acquisition function to decide where to sample next, balancing exploration of uncertain regions with exploitation of promising areas.
Update GaSP model with results for new run(s) and repeat sequence until factor settings satisfying optimization goals are discovered.

## Slide 5: Bayesian Optimization Overview
Where is it useful:
Particularly useful for complex processes that have more than one optima
Frequently used with deterministic processes but now seeing use with real-world physical processes with noise
  Machine Learning: It excels at tuning hyperparameters for complex models, such as deep neural networks, where training each configuration can take a very long time.
  Materials Science and Chemistry: Researchers use it to find new materials with desired properties, such as stronger concrete or new dye laser molecules, by efficiently guiding experimental trials.
  Robotics: It can be used to find optimal parameters for robotic movements, such as designing the gait for a locomotive robot.
  Hardware Design: It helps in optimizing design parameters and heuristics for hardware, balancing performance and efficiency.
  Recommender Systems: It can be used to tune the parameters of recommender systems to improve user recommendations.

## Slide 6: Bayesian Optimization Overview
Potential gotchas:
Can’t find an optimum if it doesn’t exist – still need subject matter expertise to set reasonable goals
When using with stochastic processes, if factor ranges are too narrow (so factors generate small effects) acquisition functions may not converge – i.e., it is hard to find an optimum in processes with small S/N ratios
When goals are targets rather than maxima or minima, too tight a target range will overly constrain or “trap” the max desirability optimum making it difficult to achieve the non-target goals
Optimization may run into the end of factor ranges, suggesting that ranges be extended to see if these new regions lead to better performance

## Slide 7: Complex Process with Multiple Minima

## Slide 8: How are Space-Filling Designs Different from Traditional Designs?
Rather than emphasizing high leverage trials (“corners”) for a simple polynomial model, space-filling designs “spread” their trials more uniformly through the space to better capture the local complexities of the simulation model.

## Slide 9: Active Learning Symposium 2025
T
Online November 24th. Recording coming soon.
Featured these open-source Bayesian Optimization tools:
Brownie Bee software is an open-source and browser-based tool developed by the Danish Technological Institute (DTI), in collaboration with Novo Nordisk and The Alexandra Institute, to help companies optimize industrial processes using advanced mathematics.
Bayesian Back End (BayBE) is an open-source toolbox by Merck KGaA for Bayesian optimization, featuring custom encodings, chemical knowledge integration, hybrid spaces, transfer learning, simulation tools, and robust, serializable code for real-world experimental campaigns.
Honegumi is a user-friendly, interactive tool designed to simplify the process of creating advanced Bayesian optimization scripts. (Built on Ax which is built on BoTorch and GPyTorch libraries.)

## Slide 10
https://github.com/materials-data-facility/awesome-bayesian-optimization
Twenty-one actively maintained open-source Bayesian Optimization packages on GitHub:
Adaptive Experimentation Platform (Ax) is a user-friendly, modular, and actively developed general-purpose Bayesian optimization platform with support for simple and advanced optimization tasks such as noisy, multi-objective, multi-task, multi-fidelity, batch, high-dimensional, linearly constrained, nonlinearly constrained, mixed continuous/discrete/categorical, and contextual Bayesian optimization.
BoTorch is the backbone that makes up the Ax platform and allows for greater customization and specialized algorithms such as risk-averse Bayesian optimization and constraint active search.
Dragonfly is an open-source python library for scalable Bayesian optimization with multi-objective and multi-fidelity support.
RayTune offers experiment execution and hyperparameter tuning at any scale with many supported search algorithms and trial schedulers under a common interface.
Aspuru-Guzik Group
  Atlas is a Python package that offers Bayesian optimization tailored towards real-world experimental science problems: mixed parameters, multi-objective, noisy, constrained, multi-fidelity, and meta-learning optimization along with search space expansion/contraction. [WIP]
  Chimera is a hierarchy-based multi-objective optimization scalarizing function.
  Gryffin enables Bayesian optimization of continuous and categorical variables with support for physicochemical descriptors and batch optimization.
  Gemini is a scalable multi-fidelity Bayesian optimization technique and is supported by Gryffin.
  Golem is an algorithm that helps identify optimal solutions that are robust to input uncertainty (i.e., robust optimization).
  Phoenics is a linear-scaling Bayesian optimization algorithm with support for batch and periodic parameter optimization.
  Anubis is a Bayesian optimization algorithm that models unknown feasibility constraints and incorporates it into the acquisition function
BoFire is a Bayesian Optimization Framework Intended for Real Experiments (under development) with support for advanced optimization tasks such as mixed variables, multiple objectives, and generic constraints.
NIMS-OS is a Python package (+GUI) for workflow orchestration and multi-objective optimization software that supports BLOX, PDC, random exploration, and a multi-objective variant of PHYSBO.
SLAMD - A web app leveraging data-driven design for cementitious materials via a digital lab twin, complemented by a (materials-agnostic) AI optimization feature. Features UI to interactively explore design spaces. The web app uses Python and Javascript.
Summit is a set of tools for optimizing chemical processes with a wide variety of design of experiments (DoE) and adaptive design methods along with benchmarks.
GPax is a Python package for physics-based Gaussian processes (GPs) built on top of NumPyro and JAX that take advantage of prior physical knowledge and different data modalities for active learning and Bayesian optimization. It supports "deep kernel learning", structured probabilistic mean functions, hypothesis learning workflows, multitask, multifidelity, heteroscedastic, and vector BO and emphasizes user friendliness.
Bayesian Back End (BayBE) is an open-source toolbox by Merck KGaA for Bayesian optimization, featuring custom encodings, chemical knowledge integration, hybrid spaces, transfer learning, simulation tools, and robust, serializable code for real-world experimental campaigns.
Bayesian-Optimization Pure Python implementation of Bayesian global optimization with gaussian processes.
GPFLow GPflow is a package for building Gaussian process models in python, using TensorFlow.
Spearmint: A well-known implementation of Bayesian optimization that has been around for some time and incorporates advancements in the field.
BOXVIA: A GUI-based application from NASA that allows users to perform Bayesian optimization without extensive programming skills and includes visualization tools for interpreting results.

## Slide 11: Bayesian Optimization Overview
Cold Start
No Existing Data
Model Responses
Goals Met?
Determine
Next Run(s)
Collect Responses
Starting Design
No
Yes
Finished
Warm Start with Existing Data
Gaussian Process Model (GaSP)
Acquisition Functions
guide search, optimizing balance between exploration & exploitation
Max Expected Improvement, Space-Filling DOE, Max Desirability,
and others

## Slide 12: Bayesian Optimization
  Pure Exploration, maximizing prediction variance,
    Improves model fit
    Isn’t directly related to the problem at hand
    Gives too much attention to uninteresting regions
    Exactly the application of D-optimality in DoE to GaSP
  Pure Exploitation, always optimizing current model,
    Doesn’t necessarily improve model fit
    Bad models lead to suboptimal decisions
    Exploitation gets stuck by itself
    Same as optimization with the Profiler

## Slide 13: Bayesian Optimization
  Acquisition Functions – Trade off Exploration vs Exploitation
    Expected Improvement
    Upper Confidence Bound
  With noisy functions, these both overemphasize optimization early.
  We created Auto Mode phases to solve this problem

## Slide 14: Bayesian Optimization
EXPECTED IMPROVEMENT
  Improvement:
  Idea: Find the that gives the highest expected value of
Dominates
when
Dominates
when
is large
EI acquisition function recommends 1 run at a time trading off and

## Slide 15: Bayesian Optimization
Maximize a single response,
  Inputs, , are continuous
  observed with little / no error
modeled with a GaSP:
Recommends one run at a time trading off and
“BASIC” BAYESIAN OPTIMIZATION

## Slide 16: Bayesian Optimization
  : 4238.6
Notes: The factor settings with the highest expected information value is the recommended the next run.

## Slide 17: Bayesian Optimization
  : 4238.6
  Recommends X=4.79 next
Notes: The factor settings with the highest expected information value is the recommended the next run.

## Slide 18
GASP MOUNTAIN
  N=2
  : 3881.1
  @ X=1.61
Bayesian Optimization
Notes: Here is a simple example. The true function we want to maximize is overlain in blue in the middle profiler panel. This is a pretend example because in real problems we can’t see the true function. Notice it is a multi modal complicated function that would be difficult to model with a classical approach.
To start we have two points. The model fit is in the middle panel with the uncertainty and data overlain. The bottom panel is the prediction variance, and the top panel is the EI acquisition function which assigns a value to every possible new point to explore, trading off potential optimal solutions to prediction uncertainty. The x value with the largest value is the next run recommended by EI. If we add a measurement at that location

## Slide 19
GASP MOUNTAIN
  N=2
  : 3881.1
  @ X=1.61
Bayesian Optimization
Notes: Here is a simple example. The true function we want to maximize is overlain in blue in the middle profiler panel. This is a pretend example because in real problems we can’t see the true function. Notice it is a multi modal complicated function that would be difficult to model with a classical approach.
To start we have two points. The model fit is in the middle panel with the uncertainty and data overlain. The bottom panel is the prediction variance, and the top panel is the EI acquisition function which assigns a value to every possible new point to explore, trading off potential optimal solutions to prediction uncertainty. The x value with the largest value is the next run recommended by EI. If we add a measurement at that location

## Slide 20
GASP MOUNTAIN
  N=3
  : 3928.1
  @ X=3.47
Bayesian Optimization
Notes: We try that point and see it led to little improvement. The expected improvement criterion next recommends a point further away with higher prediction variance

## Slide 21: Bayesian Optimization
GASP MOUNTAIN
  N=3
  : 3928.1
  @ X=3.47
Notes: We try that point and see it led to little improvement. The expected improvement criterion next recommends a point further away with higher prediction variance

## Slide 22: Bayesian Optimization
GASP MOUNTAIN
  N=4
  : 4238.6
  @ X=4.79
Notes: This one did a bit better. We continue the search in the same direction

## Slide 23: Bayesian Optimization
GASP MOUNTAIN
  N=4
  : 4238.6
  @ X=4.79
Notes: This one did a bit better. We continue the search in the same direction

## Slide 24
GASP MOUNTAIN
  N=4
  : 4238.6
  @ X=4.78
Bayesian Optimization
Notes: This one did a bit better. We continue the search in the same direction

## Slide 25: Bayesian Optimization
GASP MOUNTAIN
  N=4
  : 4238.6
  @ X=4.78
Notes: This one did a bit better. We continue the search in the same direction

## Slide 26: Bayesian Optimization
GASP MOUNTAIN
  N=5
  : 4238.6
  @ X=3.16
Notes: This time we did worse than expected, and it recommends a nearby point in the other direction

## Slide 27: Bayesian Optimization
GASP MOUNTAIN
  N=5
  : 4238.6
  @ X=3.16
Notes: This time we did worse than expected, and it recommends a nearby point in the other direction

## Slide 28: Bayesian Optimization
GASP MOUNTAIN
  N=6
  : 4287.3
  @ X=6.79
Notes: The algorithm has identified the local optima and is now recommending giving attention to the unexplored region

## Slide 29: Bayesian Optimization
GASP MOUNTAIN
  N=6
  : 4287.3
  @ X=6.79
  Pure Exploitation
  will get stuck!
Notes: The algorithm has identified the local optima and is now recommending giving attention to the unexplored region

## Slide 30: Bayesian Optimization
GASP MOUNTAIN
  N=6
  : 4287.3
  @ X=6.79
  High variance region of interest
Notes: The algorithm has identified the local optima and is now recommending giving attention to the unexplored region

## Slide 31: Bayesian Optimization
GASP MOUNTAIN
  N=6
  : 4287.3
  @ X=6.79
  EI balances all this out!
Notes: The algorithm has identified the local optima and is now recommending giving attention to the unexplored region

## Slide 32: Bayesian Optimization
GASP MOUNTAIN
  N=6
  : 4287.3
  @ X=6.79
  EI balances all this out!
Notes: The algorithm has identified the local optima and is now recommending giving attention to the unexplored region

## Slide 33: Bayesian Optimization
GASP MOUNTAIN
  N=7
  : 5261.1
  @ X=7.3
Notes: We add a point there and obtained a much better than expected result

## Slide 34: Bayesian Optimization
GASP MOUNTAIN
  N=7
  : 5261.1
  @ X=7.3
Notes: We add a point there and obtained a much better than expected result

## Slide 35: Bayesian Optimization
GASP MOUNTAIN
  N=8
  : 5261.1
  @ X=6.46
Notes: It takes another step in the same direction

## Slide 36
GASP MOUNTAIN
  N=8
  : 5261.1
  @ X=6.46
Bayesian Optimization
Notes: It takes another step in the same direction

## Slide 37
GASP MOUNTAIN
  N=9
  : 5479.6
  @ X=6.28
Bayesian Optimization
Notes: The result was lower, so the algorithm backs up

## Slide 38: Bayesian Optimization
GASP MOUNTAIN
  N=9
  : 5479.6
  @ X=6.28
Notes: The result was lower, so the algorithm backs up

## Slide 39: Bayesian Optimization
GASP MOUNTAIN
  N=10
  : 5540.3
  @ X=6.19
Notes: It has basically found the optima, and the expected improvement is low across the range of X.

## Slide 40: Bayesian Optimization
GASP MOUNTAIN
  N=10
  : 5540.3
  @ X=6.19
Notes: It has basically found the optima, and the expected improvement is low across the range of X.

## Slide 41: Bayesian Optimization
GASP MOUNTAIN
  N=11
  : 5540.3 @ X=9.0
Notes: The optima is then confirmed, and the expected improvement criterion is back to recommending high uncertainty points. Notice that the expected improvement is small everywhere, we means we can declare success in maximizing this function. This example shows how Bayesian optimization combines classical statistical thinking with machine learning to create a mathematical optimization algorithm. This idea can easily be applied in the same way to real industrial innovation applications. The approach is adaptive to the response values and goal. As a result, it indicates when your search can stop.

## Slide 42: Bayesian Optimization
  Flexible to work the way you want to:
    Easy to incorporate ad-hoc proposals
    Easy to change ranges and add variables
    Easy to fix factors, optimize others: “smart OFAT”
    Easy mixture/constraint handling

## Slide 43: Bayesian Optimization
  Faster and more efficient:
    Small starting data (8 factors, 2 starting runs!)
    Use messy initial starting data
    Work iteratively and stop when goals are met
    Using responses and goals accelerates innovation

## Slide 44: Bayesian Optimization
  Problem solving without the statistical machinery:
    No p-values, hypothesis tests, or power calcs
    Response surface emerges directly from the data
    No interaction or curvature effects to declare
    No such thing as VIFs, less concern about aliasing
    Randomization often the opposite of what you want

## Slide 45: Bayesian Optimization
  Problem solving without the statistical machinery:
    No p-values, hypothesis tests, or power calcs
    Response surface emerges directly from the data
    No interaction or curvature effects to declare
    No such thing as VIFs, less concern about aliasing
    Randomization often the opposite of what you want
  Statistical analysis is about proving things, Bayesian optimization is about improving things

## Slide 46
ITERATION HISTORY
  EI trends towards zero
  X converges: Exploration yields to exploitation

## Slide 47
ITERATION HISTORY
  Why not look around here?

## Slide 48
DECISION CONSIDERATIONS
  Practical Considerations:
  Are recent response values good enough?
  Do we trust the model ( pred & var)?
  Are we satisfied with coverage of factor space?
  If No to 2 or 3 continue exploring, else:
  Model Based Considerations:
  Is EI small?
  Is the augmentation close to the optima?
  Is the interval around EI or the optima small?
  If No to any of these, skip EI and keep exploring…

## Slide 49
STOPPING CRITERIA
  The Model doesn’t know how wrong it is

## Slide 50
STOPPING CRITERIA
  The Model doesn’t know how wrong it is
  This is especially the case when N is small and nX is large

## Slide 51
STOPPING CRITERIA
  The Model doesn’t know how wrong it is
  This is especially the case when N is small and nX is large
  It is up to you to guide the project into useful directions

## Slide 52
CONCLUSIONS
  Acquisition functions are being intensively researched
  There isn’t one best one for all situations
  It is the practitioner’s responsibility to make decisions based on:
    The quality of results, understanding any model is wrong
    The resources available
    Subject matter knowledge and practical experience
  We will work with EI for the remainder of the workshop, but the same principles apply now no matter how you proceed
  We are really proposing to have the user make a decision based on EI and varimax considerations

## Slide 53: Bayesian Optimization
Auto Mode
Uses simple, conservative run acquisition rules based on model fit and observed response values
Three Phases:
  Space-filling (Exploration)
  Refine Model (Exploitation)
  Confirm/Challenge
Custom Mode
Very flexible in terms of how to choose runs directly from the Profiler or from user-curated candidate sets
Direct user control means that you can solve problems in fewer efforts, but with some effort and subject matter knowledge
Notes: There are two modes for run selection. The first is Auto Mode, which requires very little on the part of the user once the data table is set up properly. It is intended to be somewhat conservative in that is favors spacefilling approaches until the evidence in the data appears that it is reasonable to use the model more directly
It has three modes, which I will explain as I go through the first example.
The other mode is Custom Mode. This gives the user the ability to choose runs directly using profilers of acquisition functions, and allows the user to set up their own candidate set that may satisfy constraints that are not naturally supported by JMP. You can do a lot with this, for example, you can simply change factor ranges in the profiler and determine runs using the new ranges.
Our goal here is to have an ‘easy path’ for users that don’t want to get into the details, or when the problem fairly standard and not that difficult, while giving another path that is for users that want to understand the machinery of BO in JMP and have harder problems that won’t have an easy out-of-the-box solution.

## Slide 54: Bayesian Optimization of Branin Function

## Slide 55: Bayesian Optimization
Auto Mode Rules
Are all the RSq’s larger than the threshold AND do we have any training rows compatible with the acceptable ranges of the responses?
  If no use MaxPro Space-filling criterion (Exploration)
  If yes Is there a candidate row whose confidence interval suggests it can beat the best training row?
  If yes use Refine Model - Max Expected Improvement (Exploitation)
  If no use Confirm/Challenge

## Slide 56: Bayesian Optimization of Process with 3 Responses

## Slide 57: Bayesian Optimization
Auto Mode Rules to select a batch of size k:
Space-filling Exploration: Choose k runs by sequentially maximizing the MaxPro Space-filling criterion
Refine Model: Considering only candidates consistent with the response limits:
1) Choose the Max Expected Improvement (MEI) optimal run
      2) Choose up to 2 Max Bayes Desirability Std Dev runs sequentially
      3) Choose up to k-3 runs that maximize pred variance sequentially
Confirm/Challenge: Considering only candidates consistent with best training row:
        Choose the candidate with highest Bayes Desirability
        Choose up to k-1 Max Bayes Desirability Std Dev runs sequentially

## Slide 58: Bayesian Optimization
  observed with random error
  Categorical inputs or outputs
  Missing inputs
  “Batch” augmentation of more than one run
  Many inputs:
  Adding new factors in middle of project
  Multiple responses, with
    Competing goals
    Complicated sparsity
  Match target/spec limit goal
    or
  Randomization restrictions (blocking & split plotting)
  Messy training data of unknown and dubious value
“EXOTIC” BAYESIAN OPTIMIZATION
Notes: Now in JMP we have the Profiler, which is a powerful tool for optimizing multiple responses, with different types of goals, which can be arbitrary combinations of maximizing, minimizing and matching targets. It is capable of this using desirability functions which give a score to the predicted values for each response and combines these into an overall desirability score for all the responses.
What we have done here with the new Bayesian Optimization platform in JMP Pro is combine profiler optimization via desirability functions with Bayesian optimization, the value statement being that by starting with either a very small sample from a spacefilling design or with messy historical data pulled from a database of similar projects, we can reduce the time and resources to innovate new products an processes.

## Slide 59
Recorded 2-hour workshop – Explains the “Exotic” details
*European Network for Business and Industrial Statistics
*

## Slide 60
4-minute video
*

## Slide 61: Bayesian Optimization
Adding Optimal Settings to Batch
Notes: We can use the Profiler to directly optimize these acquisition functions

## Slide 62: Bayesian Optimization
Adding Optimal Settings to Batch
Notes: We can use the Profiler to directly optimize these acquisition functions

## Slide 63: Bayesian Optimization
The “Exploration” methods
MaxPro
  Spacefilling, only based on X not the model
  Useful when the when model fit is not good
Multimodel Std Dev
  Spacefilling based on model (X & y)
  Conceptually identical to D-optimality on prediction
  More likely to explore the edges and vertices
  Less used than MaxPro / Bayes Std Dev
Bayesian Desirability Std Dev
  Spacefilling based on model & goals (X & y & Goals)
  D-optimality to learn Bayesian Desirability
  Finds “interesting” unexplored regions
  Ignores “uninteresting” regions
Notes: From there we use Gauss-Hermite quadrature to calculate the mean and variance of the responses desirability functions incorporating the desirability weight. From there we use the rule for calculating the mean and variance of products of independent random variables. This is how we combine all the response models together into a simple single response Bayesian Optimization problem.

## Slide 64: Bayesian Optimization
The “Exploitation” methods
MEI
Upper Confidence Bound (UCB)
Both work off the Bayesian Desirability rather than the prediction formulas
There is better theory for UCB, but MEI is better known
Notes: From there we use Gauss-Hermite quadrature to calculate the mean and variance of the responses desirability functions incorporating the desirability weight. From there we use the rule for calculating the mean and variance of products of independent random variables. This is how we combine all the response models together into a simple single response Bayesian Optimization problem.

## Slide 65: Bayesian Optimization
Convenient way to reset the Profiler to the best training run
Assess the “current” state of the art responses & goals
Useful to force replication of the best settings
Confirm/Challenge
Notes: From there we use Gauss-Hermite quadrature to calculate the mean and variance of the responses desirability functions incorporating the desirability weight. From there we use the rule for calculating the mean and variance of products of independent random variables. This is how we combine all the response models together into a simple single response Bayesian Optimization problem.

## Slide 66: Bayesian Optimization Benefits/Value
Small starting designs - stop when goals are met - reduce time & expense
Ease of adoption compared to many classical statistical methods for process optimization - statistically simpler: no p-values, normality tests, etc.
Response surface shape emerges naturally from the Gaussian Process model
  No need to do effect selection to determine the form of the model (i.e., interactions, curvature)
Guided iterative approach aligns naturally with how process development engineers think
Accounts for response goals and existing factor space, then optimizes
While computationally complex, results are easy to digest and interpret
  Couple of reminders…
  1. Statistical analysis is about proving things, Bayesian optimization is about improving things
  2. Garbage In – Garbage Out!

## Slide 67: Thanks to my colleagues
Charlie Whitman
Byron Wingerd
Greg Flexman
Ben Barosso-Ingham
Mike Anderson
Peter Polito
Sarah Gilyard
Bradley Bowen
Phil Kay
Peter Hersh

## Slide 68: Back Up Slides
Full slide deck follows for the 2-hour workshop presented by Chris Gotwalt on December 18, 2024, for the European Network for Business and Industrial Statistics (ENBIS).

## Slide 69
BAYESIAN OPTIMIZATION:
A Goal Oriented Approach
to Process Optimization
Notes: Now I will transition to something coming in JMP Pro 19, Bayesian Optimization. This is a very promising approach that is getting a lot of attention as an AI recommender system for improving products and processes.
It is too early to show the new platform, but I will introduce you to the idea of Bayesian Optimization, why it is so exciting, and talk about our goals for JMP Pro 19.

## Slide 70
Innovation is the key to economic growth in advanced economies:
  Product formulation for pharma, consumer products, materials
  Process innovation in semiconductor manufacturing
  Design of mechanical devices: engines, machines, motors
Competitive Innovation Pressure demands companies to innovate quickly to be the first to market
BAYESIAN OPTIMIZATION INTRO

## Slide 71
BAYESIAN OPTIMIZATION INTRO
Bayesian Optimization:
  Is an integrated modeling/data augmentation methodology
  Has the potential to have a transformative impact on innovation
  Agile product development
  Easier adoption by SMEs ( AI Recommenders are cool)
  Head start leveraging existing R&D data lakes
  Less starting runs, less total runs
  Reduce R&D costs & time-to-market
  3) BO’s iterative “filling in the knowledge gaps” approach is highly psychologically appealing to industrial R&D culture

## Slide 72
BAYESIAN OPTIMIZATION
Bayesian optimization will be easy to learn and use:
  Less statistical machinery:
    No p-values, hypothesis tests, or power calculations
  Response surface emerges directly from the data:
    No need to plan in advance for interaction or curvature effects
  Requires less resources:
    Small starting designs (8 factors, 2 starting runs!)
    Work iteratively and stop as soon as your goals are met
    Integrating all the information with product goals accelerates innovation
Notes: I believe Bayesian Optimization can be made easy to learn and use: there are fewer assumptions, with more time spent learning problem solving rather than statistical machinery like p values and power calculations
Linear statistical models concepts like interactions and curvature terms are much less important, because the machine learning algorithm learns the shape of the response surface directly from the data
Bayesian optimization is appealing because it requires only a very small initial data set and uses less resources because it goal oriented and uses all the information available.

## Slide 73
BAYESIAN OPTIMIZATION
Introduction to Bayesian Optimization (BO)
Gaussian Process Models Overview
Intro to JMP (with Phil Kay)
Bayesian Optimization Augmentation (with Chris Gotwalt)
Case Study (with Phil Kay)

## Slide 74
BAYESIAN OPTIMIZATION INTRO
About Me:
  Lead the Statistics Modeling Dev, Testing, Doc teams for JMP
  Developed a lot of the linear algebra, numerical optimization, numerical integration and fitting routines
  Mixed Models, Neural Networks, SEM, SVM, early in my career I did optimal design and reliability model fitting algorithm development
  We have a “working management” culture in JMP R&D. I am still an algorithms developer
  Almost all JMP statistical capabilities are built from scratch in C++

## Slide 75
About Me:
  Outreach working directly with customers, developing initial training material
  Become involved in high value new initiatives to lead and contribute
  In 2023 customer meetings and conferences like ENBIS and JMP Discovery led me to believe BO is the most important new thing we must develop
  Nearly every one of our customers has asked us “what is your BO solution and when can we have it?”
BAYESIAN OPTIMIZATION INTRO

## Slide 76
BAYESIAN OPTIMIZATION
Introduction to Bayesian Optimization (BO)
Gaussian Process Models Overview
Intro to JMP (with Phil Kay)
Bayesian Optimization Augmentation (with Chris Gotwalt)
Case Study (with Phil Kay)

## Slide 77
BAYESIAN OPTIMIZATION
Notes: Bayesian optimization begins by identifying responses that quantify the objectives of the talk at hand, as well as goals like maximizing them, minimizing them, or matching a target value for them.
Then you obtain some data, either starting with observed or historical data or by running an initial starting design. Once you have the data you fit a model using the inputs to predict the responses. This is where the process is in the JMP profiler plot we see here. There are three factors being used to predict three responses, one of which we want to maximize, and two other we want to match to a particular value. The model traces are shown in black, and the grey regions are the confidence intervals on the predictions. This type of graph is called the Profiler in JMP and is a very powerful tool for using models to solve real problems.
Up to this point Bayesian optimization is just like any other statistical or machine learning modeling procedure or DoE. Where it differs is in how we choose which factor combinations to try next.

## Slide 78
BAYESIAN OPTIMIZATION
Model Predictions
Notes: In that you use the model predictions based on fitting the model to the observed response values

## Slide 79
BAYESIAN OPTIMIZATION
Prediction Uncertainty
{
+
Model Predictions
Notes: Along with the prediction uncertainty from the model, which will generally differ at different factor combinations.

## Slide 80
BAYESIAN OPTIMIZATION
Prediction Uncertainty
Model Goals
{
+
+
Model Predictions
Notes: And incorporate the goals you have for the responses, shown here as desirability functions

## Slide 81
BAYESIAN OPTIMIZATION
Model Predictions
Prediction Uncertainty
Model Goals
{
+
+
=
New Factor Combinations to Try
{
Notes: These three components are combined using what are called acquisition functions that identify the most promising new combinations of the inputs to try to optimize your responses in the next iteration.

## Slide 82
POPULAR INNOVATION STRATEGIES IN INDUSTRY
Existing data-centric procedures for product/process innovation
  Subject Matter Expert driven, ad hoc “artisanal” approaches
  Design of Experiments (DoE)
Notes: Now lets review two of the most common approaches to design products and processes in industry

## Slide 83
Subject Matter Expert driven, “artisanal” approaches
  Trial and error, using the knowledge and experience of an expert
  Often falls into the trap of one factor at a time experimentation
  Uncertainty is not quantified
  Blind spots in the data are often unidentified and unresolved (thereby inefficient and suboptimal)
  Practitioner feels in control, but often hard work leads to no payoff
BAYESIAN OPTIMIZATION INTRO

## Slide 84
Design of Experiments (DoE)/ Box Hunter & Hunter (BH2) further developed by many people (e.g. Brad Jones, Peter Goos, Chris Nachtsheim)
  Consult with the expert to define goals and factor ranges
  Run a screening design to identify important factors
  Augment via replicates, foldovers, or optimality criteria
    Resolve interactions
    Accommodate curvature
    Improve precision in estimates
  Fit a final response surface model and optimize
BAYESIAN OPTIMIZATION INTRO

## Slide 85
BAYESIAN OPTIMIZATION INTRO
Classical BH2 Design of Experiments (DoE)
  Built-in handling of variation and uncertainty quantification
  Augmentation addresses linear model weaknesses:
    Estimability of interactions and curvature
    Improving precision via functions of
  Augmentation is statistically motivated:
    Does not leverage the response values!
    Does not incorporate the goals
    Places points at extremes and centers of ranges (because)

## Slide 86
BAYESIAN OPTIMIZATION INTRO
Classical BH2 Design of Experiments (DoE)
  Has had tremendous success for 50+ years, which will certainly continue
  BH2 is safe with decades of experience regarding:
    How to set up DoE’s, evaluate, and analyze them
    How they can fail and be improved with more runs
    Lots of well-established books and training material on DoE
  Many potential R&D practitioners have had criticisms:
    Large up-front sample size requirements
    Focus on statistical issues as opposed to problem solving

## Slide 87
Bayesian Optimization is a mathematical optimization algorithm:
  Find settings, that maximize (or minimize)
BO selects new ’s using Acquisition Rules that combine:
  , a data-derived model
  , the estimated precision of
  Goal for goal: augmentation is problem solving oriented
BAYESIAN OPTIMIZATION

## Slide 88
“BASIC” BAYESIAN OPTIMIZATION
  Have data : single continuous response, continuous inputs
  Obtain model along with
  The Acquisition Function , places a numeric value on all candidate ’s to try.
  We perform a search (somehow…) to find the with the best value of the Acquisition.
  Obtain , update model, and repeat until satisfied

## Slide 89
“EXOTIC” BAYESIAN OPTIMIZATION
  observed with random error
  Categorical inputs or outputs
  Missing inputs
  “Batch” augmentation of more than one run
  Many inputs:
  Multiple responses, with
    Competing goals
    Complicated sparsity
  Match target/spec limit goal
    or
  Randomization restrictions (blocking & split plotting)
  Messy training data of unknown and dubious value

## Slide 90
“EXOTIC” BAYESIAN OPTIMIZATION
  Every example I have seen has been “Exotic” in multiple ways

## Slide 91
  The methodology for common types of “exoticness” is not mature
  I know of several companies that have spent $100k-$250k for consulting on single BO projects, and have been disappointed
  Diagnostics for when things are going wrong and what to do then are not mature
  Often Gaussian Process models are the base learner, these are numerically slow and can be “temperamental”
  Inference is not the focus (but uncertainty quantification still is)
BAYESIAN OPTIMIZATION (POTENTIAL) DISADVANTAGES
Notes: I have already talked about the potential advantages of BO, much of which centers around the lack of maturity in the approach.
Several companies I know of have spent large sums to vendors for single projects that went nowhere, and have come to us looking for a better and more transparent way of doing Bayesian optimization.
BO doesn’t have the rich set of diagnostics that have been worked out for linear statistical models to identify when things are going wrong.
Gaussian Process models can be difficult to work with, although we are working hard on that right now.

## Slide 92
THIS WORKSHOP
  We will be focusing on “Basic” BO, but with error in y.
    Single continuous response
    Continuous inputs
  The modeling family will be Gaussian Process regression
    GaSP models are flexible and have a convenient for BO with a natural extension to batch augmentation
    GaSP interpretability is less than linear models, but higher than pure ML models like NN’s and Tree-based models

## Slide 93
  BO coming in JMP Pro 19. Developed by Kasia Dobrzycka and contributions from myself
  Empower SMEs in industrial R&D (like 6 Black Belts) to design products and processes w BO efficiently, effectively and safely
  Decision process: Comprehendible, transparent, reproducible, trustworthy, and easily trainable to non-expert, intermittent users
  Handling of multiple responses with complex sparsity, with different goals ( including matching targets )
  Batch augmentation
JMP Pro 19 Roadmap

## Slide 94
JMP® Student Edition
Free single-user 12-month license
JMP Student Edition is a free, comprehensive statistical analysis and visualization tool designed for classroom instruction. Based on the powerful JMP Pro software, it offers a user-friendly interface and a wide range of capabilities for teaching and learning statistical concepts.
Ideal for both introductory and advanced statistics courses, JMP Student Edition provides access to a variety of statistical techniques and graphical tools. It’s perfect for demonstrating statistical principles, analyzing real-world data, and helping students develop critical thinking skills.

## Slide 95
WE ARE AT THE BEGINNING
  BO fits squarely in the industrial product/process innovation space
  The techniques are squarely in the realm of statistical modeling and design (it is both a neural network and a linear mixed model, augmentation principles are closely related to G-optimality)
  This will have a transformative disruptive effect. BO in some form will occupy an important place in industry in the future
  This is a call to action for the industrial statistics community.
  We (the stats community) must take the lead, if not others will

## Slide 96
BAYESIAN OPTIMIZATION
Model Responses
Goals Met?
Determine
Next Run(s)
Collect Responses
No
Yes
Finished
Starting Design or
Existing Data
BO Acquisition Function
(such as Expected Improvement)
Gaussian Process Model (GaSP)
Notes: The workflow is an iterative process of data collection and modeling with Gaussian Processes, followed by using acquisition functions such as expected improvement to identify factor combinations to try next.

## Slide 97
BAYESIAN OPTIMIZATION
Introduction to Bayesian Optimization (BO)
Gaussian Process Models Overview
Intro to JMP (with Phil Kay)
Bayesian Optimization Augmentation (with Chris Gotwalt)
Case Study (with Phil Kay)

## Slide 98
GaSP PRIOR
The “Prior” in BO is that the response surface comes from a Gaussian Process
Notes: The “Prior” in BO is that mean function of the data are a continuous gaussian stochastic process

## Slide 99
GaSP MOUNTAIN
Want to predict altitude using a small number of measurements
Notes: [Introduce GaSP Mountain]. Ultimately we want to model altitude as a function of location. We know that location and altitude are closely related to one another. So we should be able to find a way to predict altitude using location

## Slide 100
GaSP MOUNTAIN
Notes: If we knew the mean and variance of the altitude across the range of X we could use that information to come up with a one size fits all guess (using just the mean) and an uncertainty metric based on the standard deviation of altitude. This doesn’t help us make location based predictions though.

## Slide 101
1.25
.33
GaSP MOUNTAIN
Notes: Then suppose we collected equally spaced measurements every 1.25 km across the range of X. We calculate their autocorrelation and find that it is equal to .33.

## Slide 102
.72
GaSP MOUNTAIN
Notes: Then we halve the interval widths and find that that autocorrelation is .72, much higher than at a stepsize of 1.25.

## Slide 103
.91
GaSP MOUNTAIN

## Slide 104
.97
GaSP MOUNTAIN

## Slide 105
.98
GaSP MOUNTAIN

## Slide 106
.994
GaSP MOUNTAIN

## Slide 107
.997
GaSP MOUNTAIN
Notes: Ultimately we find that points very near to one another are basically perfectly correlated. So, we should be able to predict locations near a measurement with high accuracy

## Slide 108
Can we:
Take a small set of points
Model the distance-correlation relationship
Combine the correlation model and the data to model y(x)?
This is the essence of Gaussian Process modeling!
GaSP MOUNTAIN
Notes: This suggest an approach we can take to do just that without taking an enormous number of measurements

## Slide 109
Consider single point prediction of given
with
We can use the conditional distribution as our model for :
GaSP MOUNTAIN

## Slide 110
GaSP MOUNTAIN

## Slide 111
GaSP MOUNTAIN
Predict given

## Slide 112
.905
GaSP MOUNTAIN
Predict given

## Slide 113
.905
=4940
GaSP MOUNTAIN

## Slide 114
.905
=4940
GaSP MOUNTAIN

## Slide 115
.905
=4940
GaSP MOUNTAIN

## Slide 116
.72
GaSP MOUNTAIN
Predict given

## Slide 117
.72
GaSP MOUNTAIN
=4790

## Slide 118
.72
GaSP MOUNTAIN
=4790

## Slide 119
For real problems we need to:
Use the data to learn the distance vs correlation relationship,
Predict using multiple points
GaSP MOUNTAIN

## Slide 120
GaSP – Gaussian Stochastic Process regression (also GP)
Predictor is linear combinations of the y’s, w/ distance-based weights
The “basic” GaSP model interpolates the data perfectly
This observation led to the use of GaSP’s as surrogate models for expensive, deterministic functions ( like computer experiments)
Prediction variance is a (scaled) distance to the rows in the data
GAUSSIAN PROCESSES

## Slide 121
is an unknown deterministic function of we want to predict
Bold terms are vectors and matrices
, : known training inputs and vector of responses
: i-th observation in the training set
: a predictor value of we want use to predict with
Here we are discussion 1-dimensional continuous x, but everything generalizes to higher dimensions and categorical x.
GAUSSIAN PROCESSES

## Slide 122
: vector correlations at x with the data,
: correlation matrix of the training data,
GAUSSIAN PROCESSES

## Slide 123
The Gaussian Correlation function is common:
  = exp(- )
  Implies that the underlying surface is infinitely differentiable
  This is often said to be “too” smooth for physical problems
There are others like the Matern family
  With these you can specify the number of derivatives that exist
  Understood that Matern is more like real physical relationships
GAUSSIAN PROCESSES

## Slide 124
and
GAUSSIAN PROCESSES

## Slide 125
Use the spatial Gaussian model to add unknown prediction point, , to the distribution of the data
Calculate the conditional distribution of given
  Application of Bayes rule in a non-Bayesian context
  Predictor is also a Mixed Model BLUP with a spatial correlation
GAUSSIAN PROCESSES

## Slide 126
GAUSSIAN PROCESSES

## Slide 127
Same structure as:
  Radial basis function (RBF) neural network
  Radial basis support vector machine
  Kernel Regression
  Spatial (Kriging) Linear Mixed Model
The “cubic” correlation function is equivalent to a spline
GAUSSIAN PROCESSES

## Slide 128
GAUSSIAN PROCESSES

## Slide 129
GAUSSIAN PROCESSES

## Slide 130
GAUSSIAN PROCESSES
-

## Slide 131
Major advantages:
  GaSP prediction learns response surface directly from data
  GaSP prediction uncertainty is based on based on scaled distance from prediction location to the data
Learning the model is based on filling gaps in the data
  “Exploration”
  “Spacefilling”
#1 Disadvantage: Slow Fitting w large n, this can be creatively mitigated
GAUSSIAN PROCESSES

## Slide 132
GaSP “EXPLORATION”
Notes: Lets see what happens as do what we call “pure exploration” by adding response data sequentially at the points where the a gaussian process model has the highest uncertainty, that is where the confidence interval on the prediction is largest. We’ll start here with just one measurement at X1=0 and add a measurement at X1=1, where the confidence interval width is widest:

## Slide 133
GaSP “EXPLORATION”

## Slide 134
GaSP “EXPLORATION”

## Slide 135
GaSP “EXPLORATION”

## Slide 136
GaSP “EXPLORATION”

## Slide 137
GaSP “EXPLORATION”

## Slide 138
GaSP “EXPLORATION”

## Slide 139
GaSP “EXPLORATION”
Notes: Here is a second example where we use spacefilling exploration to learn another function

## Slide 140
GaSP “EXPLORATION”

## Slide 141
GaSP “EXPLORATION”

## Slide 142
GaSP “EXPLORATION”

## Slide 143
GaSP “EXPLORATION”

## Slide 144
GaSP “EXPLORATION”

## Slide 145
GaSP “EXPLORATION”

## Slide 146
GaSP “EXPLORATION”

## Slide 147
GaSP “EXPLORATION”

## Slide 148
: Overall mean
  Model converges to as becomes far from data
: Smoothing parameter
  Controls rate of return to
  Indexes how far from the data the model will generalize to new
: Variance of , scales the interval width, does not change predictions
GAUSSIAN PROCESSES
Notes: Now that we have seen some gasp model predictions and how they improve with spacefilling the X region, we will use some visualizations to get some intuition for how the Gaussian Process model parameters impact the predictions and interval widths.

## Slide 149
GAUSSIAN PROCESSES
Far from the data the predictions converge to
scales the return to

## Slide 150
GAUSSIAN PROCESSES
Far from the data the predictions converge to
scales the return to

## Slide 151
GAUSSIAN PROCESSES
Far from the data the predictions converge to
scales the return to

## Slide 152
GAUSSIAN PROCESSES
is the value the model returns to far from the data

## Slide 153
GAUSSIAN PROCESSES
is the value the model returns to far from the data

## Slide 154
GAUSSIAN PROCESSES
is the value the model returns to far from the data

## Slide 155
GAUSSIAN PROCESSES
With a good model and sample size, often doesn’t impact prediction much inside the hull of

## Slide 156
GAUSSIAN PROCESSES
With a good model and sample size, often doesn’t impact prediction much inside the hull of

## Slide 157
GAUSSIAN PROCESSES
With a good model and sample size, often doesn’t impact prediction much inside the hull of

## Slide 158
GAUSSIAN PROCESSES
smooths by scaling how far an observation influences the predictions

## Slide 159
GAUSSIAN PROCESSES
smooths by scaling how far an observation influences the predictions

## Slide 160
GAUSSIAN PROCESSES
smooths by scaling how far an observation influences the predictions

## Slide 161
GAUSSIAN PROCESSES
only scales the confidence interval width without impacting predictions

## Slide 162
GAUSSIAN PROCESSES
only scales the confidence interval width without impacting predictions

## Slide 163
GAUSSIAN PROCESSES
only scales the confidence interval width without impacting predictions

## Slide 164
GaSPs WITH ERRORS
Modeling with noisy/random data requires another strategy
Notes: Unfortunately, this doesn’t work with noisy data.

## Slide 165
(the nugget) is added the diagonal of to smooth out noise
is unitless, but is analogous to measurement error
GaSPs WITH ERRORS

## Slide 166
smooths out noise by pulling predictions globally to the mean, even on
GaSPs WITH ERRORS

## Slide 167
smooths out noise by pulling predictions globally to the mean, even on
GaSPs WITH ERRORS

## Slide 168
smooths out noise by pulling predictions globally to the mean, even on
GaSPs WITH ERRORS

## Slide 169
smooths out noise by pulling predictions globally to the mean, even on
GaSPs WITH ERRORS

## Slide 170
smooths out noise by pulling predictions globally to the mean, even on
GaSPs WITH ERRORS

## Slide 171
smooths out noise by pulling predictions globally to the mean, even on
GaSPs WITH ERRORS

## Slide 172
smooths out noise by pulling predictions globally to the mean, even on
GaSPs WITH ERRORS

## Slide 173
GAUSSIAN PROCESSES
scales the correlation over distance in , smooths local to data
: smooths out the measurement error or noise, smooths globally
: center of the data and the extrapolation limit as distance grows
: Scales the prediction variance multiplicatively but leaves the predictions unchanged

## Slide 174
GAUSSIAN PROCESSES
Generalization to multiple inputs:
One parameter total, called an isotropic correlation
One parameter per dimension, called separable or anisotropic

## Slide 175
BAYESIAN OPTIMIZATION
Introduction to Bayesian Optimization (BO)
Gaussian Process Models Overview
Intro to JMP (with Phil Kay)
Bayesian Optimization Augmentation (with Chris Gotwalt)
Case Study (with Phil Kay)

## Slide 177
BAYESIAN OPTIMIZATION
Introduction to Bayesian Optimization (BO)
Gaussian Process Models Overview
Intro to JMP (with Phil Kay)
Bayesian Optimization Augmentation (with Chris Gotwalt)
Case Study (with Phil Kay)

## Slide 178
USING THE SURROGATE WITH UNCERTAINTY
  Pure Exploration, maximizing
    Improves model fit
    Isn’t directly related to the problem at hand
    Gives too much attention to uninteresting regions
  Pure Exploitation, always optimizing current
    Doesn’t necessarily improve model fit
    Bad models lead to suboptimal decisions
    Exploitation gets stuck by itself
Notes: The various strategies for augmenting tend to trade off two extremes. One we have already seen, pure exploration, augments by maximizing the point with the largest variance but it ignored the actual predicted values.
The other approach reverses this, it focuses only on optimizing the prediction model and ignored uncertainty altogether.
Focusing too much on one or the other of these strategies leads is suboptimal.

## Slide 179
USING THE SURROGATE WITH UNCERTAINTY
  Acquisition Functions – Trade off Exploration vs Exploitation
    Probability of Improvement
    Upper Confidence Bound
    Expected Improvement
  In my experience with noisy functions, these all overemphasize optimization early.
  Yes, you can add tuning parameters to make EI, etc. Explore more
  I find it more intuitive to use the mean and variance model directly in a profiler

## Slide 180
GaSP MOUNTAIN WITH 4 SAMPLES

## Slide 181
EXPECTED IMPROVEMENT
  Improvement:
  We don’t know , but we can use ) to calculate the expected value of
  Idea: Use the that gives the highest expected value of

## Slide 182
EXPECTED IMPROVEMENT
  Improvement:
  Idea: Find the that gives the highest expected value of
Dominates
when
Dominates
when
is large

## Slide 183
GaSP MOUNTAIN
Notes: Now we will apply EI as an augmentation strategy to the GaSP Mountain example with a goal of finding the location of the highest peak.

## Slide 184
  : 4238.6
BAYESIAN OPTIMIZATION
Notes: Here is a BO example with a sample of size 4 from GaSP mountain.
Expected Improvement. It assigns a value to all the possible factor combinations we could try next by balancing regions the model believes to be of high value with regions where we have high uncertainty.
You can think of it as completely analogous to looking at a set of stocks and choosing the one with the highest expected return on the investment. EI is the rate of return function across a range of X values.

## Slide 185
  : 4238.6
  Recommends X=4.79 next
BAYESIAN OPTIMIZATION
Notes: The factor settings with the highest expected information value is the recommended the next run.

## Slide 186
GASP MOUNTAIN
  N=2
  : 3881.1
  @ X=1.61
Notes: Here is a simple example. The true function we want to maximize is overlain in blue in the middle profiler panel. This is a pretend example because in real problems we can’t see the true function. Notice it is a multi modal complicated function that would be difficult to model with a classical approach.
To start we have two points. The model fit is in the middle panel with the uncertainty and data overlain. The bottom panel is the prediction variance, and the top panel is the EI acquisition function which assigns a value to every possible new point to explore, trading off potential optimal solutions to prediction uncertainty. The x value with the largest value is the next run recommended by EI. If we add a measurement at that location

## Slide 187
GASP MOUNTAIN
  N=3
  : 3928.1
  @ X=3.47
Notes: We try that point and see it led to little improvement. The expected improvement criterion next recommends a point further away with higher prediction variance

## Slide 188
GASP MOUNTAIN
  N=4
  : 4238.6
  @ X=4.78
Notes: This one did a bit better. We continue the search in the same direction

## Slide 189
GASP MOUNTAIN
  N=5
  : 4238.6
  @ X=3.16
Notes: This time we did worse than expected, and it recommends a nearby point in the other direction

## Slide 190
GASP MOUNTAIN
  N=6
  : 4287.3
  @ X=6.79
Notes: The algorithm has identified the local optima and is now recommending giving attention to the unexplored region

## Slide 191
GASP MOUNTAIN
  N=6
  : 4287.3
  @ X=6.79
  Pure Exploitation
  will get stuck!
Notes: The algorithm has identified the local optima and is now recommending giving attention to the unexplored region

## Slide 192
GASP MOUNTAIN
  N=6
  : 4287.3
  @ X=6.79
  High variance region of interest
Notes: The algorithm has identified the local optima and is now recommending giving attention to the unexplored region

## Slide 193
GASP MOUNTAIN
  N=6
  : 4287.3
  @ X=6.79
  EI balances all this out!
Notes: The algorithm has identified the local optima and is now recommending giving attention to the unexplored region

## Slide 194
GASP MOUNTAIN
  N=7
  : 5261.1
  @ X=7.3
Notes: We add a point there and obtained a much better than expected result

## Slide 195
GASP MOUNTAIN
  N=8
  : 5251.1
  @ X=6.46
Notes: It takes another step in the same direction

## Slide 196
GASP MOUNTAIN
  N=9
  : 5479.6
  @ X=6.28
Notes: The result was lower, so the algorithm backs up

## Slide 197
GASP MOUNTAIN
  N=10
  : 5540.3
  @ X=6.19
Notes: It has basically found the optima, and the expected improvement is low across the range of X.

## Slide 198
GASP MOUNTAIN
  N=10
  : 5551.1
  @ X=9.0
Notes: The optima is then confirmed, and the expected improvement criterion is back to recommending high uncertainty points. Notice that the expected improvement is small everywhere, we means we can declare success in maximizing this function. This example shows how Bayesian optimization combines classical statistical thinking with machine learning to create a mathematical optimization algorithm. This idea can easily be applied in the same way to real industrial innovation applications. The approach is adaptive to the response values and goal. As a result, it indicates when your search can stop.

## Slide 199
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
  Once the model looks reasonable the intervals EI & Var Max are non overlapping we consider the model over a “trust region” of the Xs that contains the max predicted value.
  This is inspired by “trust region” methods in Newton’s method that restrict the search to “trust” regions where the approximating quadratic is “trusted”
  As we gain more information the “trust” region will shrink for the important factors.
  We stop when we:
    Believe the model is reasonable
    The EI point is nearly identical to the predicted optimal point
    The region of the X’s whose CI is consistent with the optima is “small”

## Slide 200
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
  Original Ranges
  Optimal EI Point
  Suppose the new EI Point is close to the previous one
  Trust Region: X range whose CI contain the EI Optimal prediction
  Select varimax point in Trust Region

## Slide 201
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
  This is a one-run-at-a-time greedy algorithm for optimizing noisy physical phenomena
  The approach is very visual and places the choice for the next point completely in the hands of the practitioner.
  On simulated data based on larger real dataset, I have been able to optimize responses in much fewer runs than standard DoE approaches.
  This is a very much work in progress that while promising, can certainly be improved (hence TRBO v0.1)
  In six months, this will have likely evolved and improved (hopefully) a lot

## Slide 202
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
  Three kinds of new runs
    Pure Explore Runs: chosen because the maximize the variance of prediction (varimax) on the whole design space. All early runs are like this until the model begins to behave
    Expected Improvement Runs: These maximize EI, and should be used only once there is a clear signal in the model
    Trust Region Varimax Runs: Find the X ranges whose CI’s contain the EI prediction. Choose the point with the highest prediction variance in the region. These are done to prevent redundant EI and Pure Exploitation runs
  As long as you are challenging the model with varimax runs the model will improve. EI makes it possible to “zero in” on regions of interest.

## Slide 203
Factors Silica, Silane, Sulfur, tire rubber ingredients
Want to maximize Abrasion response
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1

## Slide 204
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
Notes: I’ll be using an JMP Add-in written by Mark Bailey that we have been using to prototupe BO in JMP. The addin requires JMP Pro, but as I mentioned academics can get JMP Pro for free any time by downloading it from the JMP website.

## Slide 205
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1

## Slide 206
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
Model traces look reasonable at EI Point, high variance, but LOO Actual By Predicted doesn’t look good -> Pure Explore

## Slide 207
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
Select Pure Exploration and Save Run to augment

## Slide 208
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
Row is added with iteration and type of point added
Select recent point to highlight it in the next graph

## Slide 209
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1

## Slide 210
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
Use recall to rerun the model

## Slide 211
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
Use recall to rerun the model

## Slide 212
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
Model traces look reasonable, overstated precision
EI and Pure Explore intervals overlap -> Try Pure Explore Point

## Slide 213
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1

## Slide 214
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
Model traces look reasonable, overstated precision
EI and Pure Explore intervals overlap -> Try Pure Explore Point

## Slide 215
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1

## Slide 216
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
Model traces look reasonable,
Highly overstated precision -> Try Pure Explore Point

## Slide 217
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1

## Slide 218
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
Model traces look reasonable
EI and Pure Explore Cis far apart -> Try EI Point

## Slide 219
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1

## Slide 220
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1

## Slide 221
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
Model traces look reasonable
EI is going for the same settings. Zoom into Trust Region and maximize Prediction Variance

## Slide 222
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
Find Factor Ranges that are totally within the CI
This is the Trust Region
Notes: [PLAY MOVIE]

## Slide 223
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
Within that Trust Region maximize the Prediction Variance

## Slide 224
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
Within that Trust Region maximize the Prediction Variance
In this case it is just the EI Optimal point

## Slide 225
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1

## Slide 226
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1

## Slide 227
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1

## Slide 228
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1

## Slide 229
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
Model is looking good at EI Point, but very narrow CI.
->Try Another Trust Region Step

## Slide 230
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1

## Slide 231
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1

## Slide 232
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1

## Slide 233
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
Model is looking good at EI Point, but very narrow CI.
->Try Another Trust Region Step

## Slide 234
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1

## Slide 235
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1

## Slide 236
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
Model is tight at EI Point, and has been consistent the last few runs. This is our proposed Optima

## Slide 237
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1
We have recovered the true optima quite well in 11 runs.

## Slide 238
TRBO – TRUST REGION BAYESIAN OPTIMIZATION v 0.1

## Slide 239
BAYESIAN OPTIMIZATION
Introduction to Bayesian Optimization (BO)
Gaussian Process Models Overview
Intro to JMP (with Phil Kay)
Bayesian Optimization Augmentation (with Chris Gotwalt)
Case Study (with Phil Kay)