## Slide 1: Cyber Testing Embedded Systems with Digital Twins
Reverse engineering, testing and vulnerability analysis
using full system simulation
DATAWorks 2023

## Slide 2: RESim Goals
Identify & analyze software that executes on embedded systems
Reverse engineer protocols used by services on those systems
Discover and analyze potential vulnerabilities, e.g., via fuzzing
Unknown systems (black box) and systems we should know

## Slide 3: Reverse engineering multiple parts of a system
What programs run?
Network traffic consumed by programs
Inter-process communication
Vulnerability analysis

## Slide 4: Cyber testing Requires Instrumentation
Ability to observe execution under different conditions
  Code coverage (you cannot test what you do not execute)
  Anomaly detection
  Fuzzers rely on code coverage feedback
  Instrumenting software is not always easy or without side effects
Approach: Instrument the hardware instead of the software
  Simulated hardware models can be easily instrumented
  Run target software unaltered within native(ish) environment

## Slide 5: High Fidelity Full System Simulation
Extract firmware/SW from media and execute within a simulation
  Not virtual machines
  Not individual computer emulators like QEMU
  Complete digital twin of networked system hardware in one simulation
Multiple simulated computers boot & interact as on real hardware
  The software is exactly that of the real system
  The hardware is a simulated, e.g., memory, registers, peripherals
With a simulated network of computers:
  Pause, step & reverse – with the entire system in lockstep
  Liberally instrument to discover what the software is doing

## Slide 6: Simics: A full system simulator
Commercial product widely used for over 25 years
Available from Wind River, has large investment by Intel
Used by chip vendors to test new hw/firmware/software pre-fab
Other uses include DevOps by software developers
No publicly described use as an RE platform
  Product focused on testing known software
  Challenge: use it to discover behavior of unknown software

## Slide 7: A View from the Other Side of the Hardware

## Slide 8: How Do We Introspect Applications?
0xFFFFFFFF
0x0
Model of RAM
Model of CPU
Target Executing Applications and Kernel
Simulator
?

## Slide 9: Lots of Breakpoints & Callbacks
0xFFFFFFFF
0x0
Syscall entry
Model of RAM
Model of CPU
Target Executing Applications and Kernel
Syscall return
Current Task
RESim callback scripts
Mode switch
Faults
Simulator
?

## Slide 10: DARPA Cyber Grand Challenge (CGC)
DEF CON style head-to-head capture the flag competition
Competitors must host network services having deliberate flaws
  Find the flaw and fix it so your service does not get compromised
  Turn the flaw into an exploit and compromise other team’s services
DARPA twist: have computers compete instead of people
  Autonomously analyze services, deploy patches and generate exploits
  Final event hosted on DARPA infrastructure at DEF CON 2016

## Slide 11: CGC Competition Integrity
Competition infrastructure development team – 3 year effort
  Team members familiar with Simics for RE in other environments
  Explored hosting competition on a simulation as an integrity check
Decision to use Simics to vet all CGC competitor software
  Built software that instruments Simics to monitor software behavior
  Extended to analyze successful exploits from the competition
CGC code base was a huge head start toward creating RESim

## Slide 12: RESim Features
System execution tracing
  System call tracing with de-referenced parameters
  Identifies processes, network connections, IPC, etc.
Dynamic analysis of processes
  IDA Pro & Ghidra plugins to control execution, e.g., breakpoints
  Ability to run forwards or backwards to system events
  Track ingested data through memory transactions and IPC
  Reverse track sources of memory or registers
AFL Fuzzer integrated with RESim for vulnerability analysis
  Inject data directly into application or kernel memory
  Run target to the desired starting state rather than building test harnesses

## Slide 13: Fuzzing –Brief Introduction
Test software by feeding it semi-random inputs
Look for faults or crashes
Discover new execution paths and behavior
A primary tool for real-word vulnerability discovery
Program
read data
parse data
do stuff with data
Fuzzer
generate semi-random data
run program and feed data
assess coverage/crashes
repeat
data
coverage crashes

## Slide 14: Fuzzing Chasm: Harnessing the Target
Goal: Monitor target application consumption of fuzzed data
Challenge: Real applications can be complicated
  Not just a simple service
  May need to interact with other processes
  May need to interact with target to bring it to desired state
Solution: Run simulation to the desired state and snapshot it

## Slide 15: Direct injection of fuzzed data
Snapshot when application has returned from a recv system call
Instrument desired basic blocks
Inject fuzzed data into application buffer & adjust returned size
Un-pause simulation and let application consume the data
  Jump over subsequent read calls and inject more data
Feed instrumentation results back to AFL
Restore snapshot and repeat (Simics in-memory snapshots)

## Slide 16: Expanding Code Coverage
Database of coverage from each fruitful AFL iteration
Find execution branches that were not taken
  Qualify search based on references to input data (separately tracked)
  Automatically bring simulation to the untaken branch point
Analyst determines if input data could lead to branch
  Feeds new data back to AFL for subsequent sessions
  Visual representation in Ghidra or IDA Pro with colored blocks

## Slide 17: Code Coverage Display in IDA Pro

## Slide 18: RESim Results
Reverse engineered several commercial maritime systems
  Analyzed protocols and functions, including undocumented ports
  Identified several vulnerabilities within network services
Basis for several masters thesis at NPS
OSD panel judged as best RFI response to next-gen simulation
Selected for USCYBERCOM CyberRecon program

## Slide 19: Summary
Cyber testing requires instrumentation
Instrumenting hardware models is a viable approach
Analyzing SW executing on simulated hardware is powerful
  Simplifies fuzzing
  Can greatly aid developmental testing and debugging
The hardware models need not be perfect
  Good enough to execute (most of) the target software
  Generic platform models are often adequate (cost/benefit)

## Slide 20: Availability / Questions
Simics runs on commodity workstations or servers
  Free version from Intel for x86 platforms
RESim & plugins for IDA Pro & Ghidra available from NPS
  Public info at https://github.com/mfthomps/RESim
RESim analyzes Linux applications on x86 and ARM
  Extend to other processors and OS’s, e.g., VxWorks, Windows
Questions?
Contact: Mike Thompson
Naval Postgraduate School
mfthomps@nps.edu