## Slide 1
Space-Filling Designs and Metamodeling for Understanding Modeling & Simulation Behavior
Curtis Miller
April 26, 2023

## Slide 2
Introduction

## Slide 3: Background
Evaluations of systems increasingly rely on M&S to supplement the data collected from live test events.
Before results from M&S are used in DOT&E reports, we want confidence that these numbers mean something!
The process of establishing credibility and trust in a model is called Verification, Validation, and Accreditation (VV&A).
SME input is necessary but not sufficient for VV&A.
Eyeballs are not the best measurement tools for comparing numbers and identifying complex trends.
Two DOT&E memos outline these concerns.
M&S: Modeling and Simulation; SME: Subject Matter Expert

## Slide 4: Motivation
The VV&A process should provide a quantitative understanding of how accurate an M&S capability is and identify limitations of the M&S across the factor space of interest.
This requires statistical analysis techniques that can precisely model the M&S output across a set of inputs and compare those results to live test results.
This requires a data collection strategy for both the M&S and the live test data.
The right data collection strategy (test design) depends on the goal
M&S: Modeling and Simulation; VV&A: Verification, Validation, and Accreditation

## Slide 5: A metamodel is a useful product in and of itself
M&S: Modeling and Simulation; T&E: Test and Evaluation; VV&A: Verification, Validation, and Accreditation
T&E
Test Planning
Performance Prediction
VV&A
M&S
M&S Development
M&S Calibration
Operations and Planning
Wargaming
Campaign Analysis
Exercise Planning
Tactical Planning
Statistics
Parameter Estimation

## Slide 6
Motivating Example

## Slide 7: Our Toy (Motivating) Example Will Be a Paper Airplane Simulator
CLASSIC
DART
BULLDOG
WORLD RECORD PAPER AIRPLANE (WRPA)
HAMMER
HARRIER

## Slide 8: Flight Simulation
Example flight (dart)
USLWUG: Ultra-Small Light Weight Unguided Glider

## Slide 9: From a paper plane flight, we can record discrete and continuous response variables
WRPA: World Record Paper Airplane

## Slide 10: From a paper plane flight, we can record discrete and continuous response variables
Loop
Bumps
Range
WRPA: World Record Paper Airplane

## Slide 11: Model, Airspeed, and Angle Study
Consider a study of the effects of initial airspeed and angle of flight (continuous factors) on flight terminal range (continuous), while also looking for differences in models (a categorical factor).
WRPA: World Record Paper Airplane

## Slide 12: Model, Airspeed, and Angle Study
Consider a study of the effects of initial airspeed and angle of flight (continuous factors) on flight terminal range (continuous), while also looking for differences in models (a categorical factor).
TWO LOCAL EXTREMA
GLOBAL MAXIMUM
SURFACE “RIDGES”
NONLINEAR INCREASE
NUMERICAL ARTIFACTS
WRPA: World Record Paper Airplane

## Slide 13: Model, Airspeed, and Angle Study

## Slide 14: Our simulation becomes random when we randomize the inputs
DETERMINISTIC
STOCHASTIC (RANDOM)
Randomize initial conditions for random output (i.e. variance in toss)

## Slide 15
Space-Filling Designs

## Slide 16: Space-filling design of experiments helps recover more trends in simulation outputs
A factorial design with a simple linear model fitted will not accurately describe the M&S system’s behavior.
M&S: Modeling and Simulation; SFD: Space-Filling Design; WRPA: World Record Paper Airplane
True response surface of simulated projectile range
Initial airspeed (m/s)
Initial angle (radians)
Estimated response surface of simulated projectile range
Initial airspeed (m/s)
Initial angle (radians)

## Slide 17: Space-filling design of experiments helps recover more trends in simulation outputs
A factorial design with a simple linear model fitted will not accurately describe the M&S system’s behavior.
M&S: Modeling and Simulation; SFD: Space-Filling Design; WRPA: World Record Paper Airplane
True response surface of simulated projectile range
Initial airspeed (m/s)
Initial angle (radians)
Estimated response surface of simulated projectile range
Initial airspeed (m/s)
Initial angle (radians)
TOO SMOOTH
INCREASES FOREVER
NOT TRUE MAXIMUM
INTERIOR PREDICTIONS TERRIBLE
Notes: Remember to talk about how power will not describe our inability to detect interior nonlinearities, or that there are interesting phenomena we want to discover that simply are not covered by thinking about power alone. “We care about power, and a lot of things other than power. Power is not everything.”

## Slide 18: Space-filling design of experiments helps recover more trends in simulation outputs
True response surface of simulated projectile range
Initial airspeed (m/s)
Initial angle (radians)
Estimated response surface of simulated projectile range
Initial airspeed (m/s)
Initial angle (radians)
Analyzing the flights with a Gaussian Process model via a Space-Filling Design yields a good approximation to simulation output.
GP: Gaussian Process; SFD: Space-Filling Design; WRPA: World Record Paper Airplane

## Slide 19: Space-Filling design of experiments helps recover more trends in simulation outputs
True response surface of simulated projectile range
Initial airspeed (m/s)
Initial angle (radians)
Estimated response surface of simulated projectile range
Initial airspeed (m/s)
Initial angle (radians)
Analyzing the flights with a Gaussian Process model via a Space-Filling Design yields a good approximation to simulation output.
GP: Gaussian Process; SFD: Space-Filling Design; WRPA: World Record Paper Airplane
REDISCOVERY OF LOCAL MAX
IRREGULAR INCREASE

## Slide 20: Just like with classical DOE, there are quantitative ways to evaluate a specific design
Many criteria exist, but it is particularly important that an SFD satisfy the following three criteria in order to be useful:
Point-distance: Samples are placed as far apart from each other as possible. [Maximin]
Uniformity: All regions of the design space are equally well represented. [Center L2 Discrepancy]
Projection: The design is robust to variables being collapsed. [MaxPro]
DOE: Design of Experiments; SFD: Space-Filling Design
A
B
C
D
Notes: So WHY do I claim that some of the designs on the previous slide are better than others? Just like there are measures of merit or ways to measure goodness for classical DOE (power, confidence, prediction variance, etc.) there are DIFFERENT evaluation criteria for SFD because the goals are different. We are trying to fill the space to support reconstructing a complex surface, not trying to control for noise and identify simple trends.
Explain 3 criteria. Uniformity – each box (red and blue) is approximately 25% of the space and thus should contain about 25% of the points to achieve good uniformity. You can see here that the random design does this poorly, while LHS-Maximin does this well.
Projection is all about efficiency and maximizing the information gained from your design. Oftentimes not all factors or inputs will matter. If this is the case, we still want the test points to give us useful information in the other dimensions. So for example, on the left, if X1 ends up not mattering, or 2 data points might as well be 1 data point because we only get 1 piece of information about X2. This is why factorials are bad for space filling! Similarly, if X1 ends up not mattering on the right side picture, we only get information about a small region of the X2 space. This is likely to happen for random designs that end up in clusters.

## Slide 21: We prefer maximin sliced Latin hypersquare designs (maximin SLHD) and MaxPro SFDs
Latin Hypersquare
General recommendations: Maximin (Sliced) LHD or MaxPro
SFD: Space-Filling Design

## Slide 22: We prefer maximin sliced Latin hypersquare designs (maximin SLHD) and MaxPro SFDs
Latin Hypersquare
General recommendations: Maximin (Sliced) LHD or MaxPro
SFD: Space-Filling Design
Good spread in the design space
Spread preserved if a factor is dropped
Handles a small (<5) number of categorical factors
Handles more categorical factors better, while also resembling maximin SLHD

## Slide 23: We will use maximin SLHDs when generating all M&S outputs
M&S: Modeling and Simulation; SLHD: Sliced Latin Hypersquare Design; WRPA: World Record Paper Airplane

## Slide 24: We recommend different analysis procedures based on the M&S output
GAUSSIAN PROCESS (GP)
NEAREST NEIGHBOR (NN) DECISION TREE
GENERALIZED ADDITIVE MODEL (GAM)
CONTINUOUS OUTPUT
DISCRETE OUTPUT
DETERMINISTIC
STOCHASTIC
M&S: Modeling and Simulation

## Slide 25
Stochastic Outputs

## Slide 26: An additive model fits smooth, mostly unspecified functions to the data

## Slide 27: An additive model fits smooth, mostly unspecified functions to the data
Coefficients like those in traditional linear models

## Slide 28: An additive model fits smooth, mostly unspecified functions to the data
Arbitrary smooth functions discovered from the data

## Slide 29: Generalized additive models (GAMs) allow fitting models with different response types
* Canonical link function
Distribution | Range | Common Use Case | Example Response | Link Functions ()
Normal | Unbounded | Measurement | Signed miss distance | Identity*
Bernoulli |  | Success or failure | Hit or miss | Logit,* probit (normal inverse cumulative distribution function (CDF)), complementary log-log (CLL), identity, angular
Poisson |  | Count | Number of failures in test | Log*
Negative Binomial |  | Count | Number of warnings until failure | * identity, square root
Gamma | Positive | Time to event | Time until failure; radial miss distance | Inverse,* log
Inverse Gaussian | Positive | Time to event | Time until failure | Square inverse*
Distribution | Range | Common Use Case | Example Response | 
Normal | Unbounded | Measurement | Signed miss distance | Identity*
Bernoulli |  | Success or failure | Hit or miss | Logit,* probit (normal inverse cumulative distribution function (CDF)), complementary log-log (CLL), identity, angular
Poisson |  | Count | Number of failures in test | Log*
Negative Binomial |  | Count | Number of warnings until failure | 
Gamma | Positive | Time to event | Time until failure; radial miss distance | Inverse,* log
Inverse Gaussian | Positive | Time to event | Time until failure | Square inverse*

## Slide 30: We can fit an additive model to the training data
Average Range: Dart: 9.3 m
Classic: 7.4 m
WRPA: 11.3 m
WRPA: World Record Paper Airplane

## Slide 31: We can fit an additive model to the training data
Average Range: Dart: 9.3 m
Classic: 7.4 m
WRPA: 11.3 m
Add values of functions to average range to get average range for some airspeed or angle
WRPA: World Record Paper Airplane

## Slide 32: We can fit an additive model to the training data
Average Range: Dart: 9.3 m
Classic: 7.4 m
WRPA: 11.3 m
How do we know we are not overfitting and can predict flights well?
WRPA: World Record Paper Airplane

## Slide 33: We can compare predicted values to observed values in a calibration plot

## Slide 34: We can compare predicted values to observed values in a calibration plot
Training set predicted value
Training set observed value

## Slide 35: We can compare predicted values to observed values in a calibration plot
Linear, one-to-one relationship implies expected observed values are predicted values
Scatterplot of observed and predicted values
Low spread implies small deviation between observations and predictions (a confident metamodel)

## Slide 36: We can compare predicted values to observed values in a calibration plot
Blue line represents ideal one-to-one relationship between a prediction and the observed response
Red line is a GAM fitted to observed values’ relationship with predictions
Shaded region is a confidence region for the relationship between observed and predicted
GAM: Generalized Additive Model

## Slide 37: We can do a statistical test to see if the relationship between observed and predicted values is the identity relationship
Red line is an estimate of the relationship between observed and predicted values
Conclusion: Do not reject ; insufficient evidence of metamodel miscalibration in training set

## Slide 38: We can do a statistical test to see if the relationship between observed and predicted values is the identity relationship
Red line is an estimate of the relationship between observed and predicted values
Conclusion: Do not reject ; insufficient evidence of metamodel miscalibration in training set
This is all the training set; what about OOS performance?
OOS: Out of Sample

## Slide 39: The metamodel appears to be properly calibrated in a separate set of outputs not used in fitting
Conclusion: Do not reject ; insufficient evidence of metamodel miscalibration in evaluation set

## Slide 40
Applications

## Slide 41: Without live data, metamodels allow for qualitative assessment of M&S environment performance
Average Range: Dart: 9.3 m
Classic: 7.4 m
WRPA: 11.3 m
M&S: Modeling and Simulation; WRPA: World Record Paper Airplane
THIS CAN’T BE RIGHT!

## Slide 42: Metamodels can help identify regions where testing should take place

## Slide 43: Metamodels can imply what statistical model should be used for test planning

## Slide 44
Summary

## Slide 45: Recap
To avoid putting inaccurate predictions in reports, test designs should support capturing M&S behavior and building a metamodel
  Supports predictions across tested and untested conditions
  Ability to quantify uncertainty
  Potential to save time and money by not having to re-run the M&S itself
M&S: Modeling and Simulation

## Slide 46: Resources and coming attractions
Space-Filling paper: https://testscience.org/wp-content/uploads/formidable/20/SFD_Literature_Review_Final.html
M&S Handbook: https://testscience.org/wp-content/uploads/formidable/20/Handbook-on-Statistical-Design-Analysis-Techniques-for-Modeling-Simulation-Validation-Reduced.pdf
Metamodeling paper: Public soon!
M&S: Modeling and Simulation

## Slide 47
BACKUP

## Slide 48: Different M&S architectures have characteristics influencing analysis
Simulation Environment | Acronym | Description
Digital Simulation | DSIM | A full digital representation of the physical system and intended operational environment. Can be deterministic or stochastic.
Hardware-in-the-Loop | HITL | A simulation that includes actual physical system hardware. Can be deterministic or stochastic, but often is stochastic due to the architecture of such simulations.
Software-in-the-Loop | SITL | A simulation incorporating actual physical system software. May be deterministic or stochastic.
Operator-in-the-Loop | OITL | A simulation that includes inputs and decisions from at least one operator. Highly stochastic.
M&S: Modeling and Simulation

## Slide 49: How will we analyze this data?
How will we connect the points and quantify our uncertainty of predictions between points?
The simulation outputs are not random
WRPA: World Record Paper Airplane

## Slide 50: A GP is a probability model describing random functions
COV: Covariance; GP: Gaussian Process; N: Normal

## Slide 51: A GP is a probability model describing random functions
COV: Covariance; GP: Gaussian Process; N: Normal
Random functions (mean zero, Gaussian kernel)
Brownian motion, where and (motion of a particle through a medium)

## Slide 52: A GP is a probability model describing random functions
COV: Covariance; GP: Gaussian Process; N: Normal
The mean function; mean value at each point (often 0)

## Slide 53: A GP is a probability model describing random functions
COV: Covariance; GP: Gaussian Process; N: Normal
The covariance kernel; describes the correlation between two points, thus controlling continuity and smoothness

## Slide 54: A GP is a probability model describing random functions
COV: Covariance; GP: Gaussian Process; N: Normal
Stationary process; statistical properties do not change with
Nonstationary process (variance increases with )

## Slide 55: GP interpolation is Bayesian inference on a function
GP: Gaussian Process

## Slide 56: GP interpolation is Bayesian inference on a function
GP: Gaussian Process; M&S: Modeling and Simulation
The prior: our belief about M&S output’s potential values and behavior before collecting outputs
The likelihood: how likely the M&S output is given that our belief about the output is true
The posterior: what we believe about the M&S output’s potential values after observing output

## Slide 57: GP interpolation is Bayesian inference on a function
GP: Gaussian Process

## Slide 58: GP interpolation is Bayesian inference on a function
GP: Gaussian Process

## Slide 59: GP interpolation is Bayesian inference on a function
GP: Gaussian Process

## Slide 60: GP interpolation is Bayesian inference on a function
GP: Gaussian Process
OR

## Slide 61: GP interpolation is Bayesian inference on a function
GP: Gaussian Process
OR

## Slide 62: GP interpolation is Bayesian inference on a function
GP: Gaussian Process; M&S: Modeling and Simulation
OR
Prior: any one of these functions could be the “right” function
Observe M&S output
Posterior: only functions connecting observed points could be “right”

## Slide 63: GP interpolation is Bayesian inference on a function
GP: Gaussian Process; M&S: Modeling and Simulation
OR
(Pointwise) credible regions for the function’s value under the prior
Observe M&S output
Posterior credible regions; at observed output, no uncertainty, but there is at unobserved regions

## Slide 64: GP interpolation is Bayesian inference on a function
GP: Gaussian Process
OR
This process is also known as kriging

## Slide 65: GP interpolation requires picking a family of covariance kernels
GP: Gaussian Process
Gaussian
Stationary Kernel: , where is the distance between and
Matérn
Nugget Effect

## Slide 66: We prefer the Matérn kernel as a default, using MLE for picking and , and picking via another method
GP: Gaussian Process MLE: Maximum Likelihood Estimation
Gaussian
Stationary Kernel: , where is the distance between and
Matérn
Nugget Effect

## Slide 67: We used a Matérn kernel and GP interpolation to fit the USLWUG range data
GP: Gaussian Process; USLWUG: Ultra-Small Light Weight Unguided Glider; WRPA: World Record Paper Airplane
Independent GPs for each plane design
Used Matérn kernel with (four continuous derivatives)
Included small nugget effect for easier calculations
Used R package GPfit

## Slide 68: We can obtain confidence bounds for the value of the simulator at unobserved points
WRPA: World Record Paper Airplane

## Slide 69: We can obtain confidence bounds for the value of the simulator at unobserved points
The DOE is of sufficient size and density, and the simulation smooth enough, that MOEs are narrow
DOE: Design of Experiments; MOE: Margin of Error

## Slide 70: Gaussian kernels are very smooth and depend on two parameters

## Slide 71: Gaussian kernels are very smooth and depend on two parameters
Mostly responsible for interval width; scales the kernel vertically

## Slide 72: Gaussian kernels are very smooth and depend on two parameters
Controls how correlated two points are; changes the shape of the fit, and width of intervals

## Slide 73: Matérn kernels have varying smoothness and depend on three parameters

## Slide 74: Matérn kernels have varying smoothness and depend on three parameters
and act like they do for the Gaussian kernel
controls how pointy the kernel is; this controls smoothness of GPs
GP: Gaussian Process

## Slide 75: Drawing from the Matérn kernel’s prior shows what it thinks the M&S environment’s output might look like
M&S: Modeling and Simulation

## Slide 76: Drawing from the Matérn kernel’s prior shows what it thinks the M&S environment’s output might look like
Increasing increasing smoothness
M&S: Modeling and Simulation

## Slide 77: Drawing from the Matérn kernel’s prior shows what it thinks the M&S environment’s output might look like
Increasing fewer bumps and wiggles
M&S: Modeling and Simulation

## Slide 78: The Matérn kernel offers more options for fitting M&S outputs
M&S: Modeling and Simulation

## Slide 79: The Matérn kernel offers more options for fitting M&S outputs
controls how smooth the fit is; the bigger it is, the more the kernel behaves like a Gaussian kernel
M&S: Modeling and Simulation

## Slide 80: The Matérn kernel offers more options for fitting M&S outputs
and serve similar roles to those in the Gaussian kernel
M&S: Modeling and Simulation

## Slide 81: Adding a nugget effect drops the need to interpolate M&S outputs
Reasons for a nugget effect include: making the problem numerically easier; analyzing stochastic data
M&S: Modeling and Simulation

## Slide 82: Adding a nugget effect drops the need to interpolate M&S outputs
Reasons for a nugget effect include: making the problem numerically easier; analyzing stochastic data
Take any kernel and augment it with a nugget effect
M&S: Modeling and Simulation

## Slide 83: Adding a nugget effect drops the need to interpolate M&S outputs
Reasons for a nugget effect include: making the problem numerically easier; analyzing stochastic data
The kernel becomes discontinuous at and the GP is no longer continuous; the mean no longer interpolates
GP: Gaussian Process; M&S: Modeling and Simulation

## Slide 84: Common situations can be addressed
PROBLEM
SOLUTION
The output is bounded
Transform the output (log, logit, etc.)
Some factors are categorical
Fit GPs for each combination
GP: Gaussian Process

## Slide 85: An initial linear model estimate has clear deficiencies
Added variable plots show the relationship between a factor and the response variable after removing the effects of other factors. This lets us see if the relationships between factors and the response appear right.

## Slide 86: An initial linear model estimate has clear deficiencies
Residuals tend to be negative at ends and positive in middle, a nonlinear shape; the linear relationship is likely wrong

## Slide 87: An initial linear model estimate has clear deficiencies
Residuals tend to be negative at ends and positive in middle, a nonlinear shape; the linear relationship is likely wrong

## Slide 88: An initial linear model estimate has clear deficiencies
Residuals average to zero across but not within model groups

## Slide 89: An initial linear model estimate has clear deficiencies
Can we estimate the shape of the relationship from the data instead of prescribing it?

## Slide 90: When smoothing, we assume the arbitrary function can be decomposed into other functions we know
LOESS: Locally Estimated Scatterplot Smoothing
This is the “penalized regression” approach to smoothing, not moving average smoothing as done by LOESS and other techniques

## Slide 91: When smoothing, we assume the arbitrary function can be decomposed into other functions we know
LOESS: Locally Estimated Scatterplot Smoothing
This is the “penalized regression” approach to smoothing, not moving average smoothing as done by LOESS and other techniques

## Slide 92: When smoothing, we assume the arbitrary function can be decomposed into other functions we know
The set of basis functions is called a basis; when picking this set we are picking a basis
Coefficients; we need to estimate these
Basis functions; we choose these

## Slide 93: When smoothing, we assume the arbitrary function can be decomposed into other functions we know
The set of basis functions is called a basis; when picking this set we are picking a basis
We substitute infinite with a number

## Slide 94: We add basis functions together to get a smooth fit

## Slide 95: We add basis functions together to get a smooth fit
Notice that later functions added make little changes to the sum

## Slide 96: Many basis options exist

## Slide 97: We use the least squared error principle for fitting additive models
LOESS: Locally Estimated Scatterplot Smoothing
This is the “penalized regression” approach to smoothing, not moving average smoothing as done by LOESS and other techniques

## Slide 98: We need more restrictions

## Slide 99: Least square objective alone leads to overfitting

## Slide 100: Least square objective alone leads to overfitting
Squared error is zero since this function connects all points; it has very low predictive ability and is maximum overfitting

## Slide 101: We need extra cost associated with bad fits
LOESS: Locally Estimated Scatterplot Smoothing
This is the “penalized regression” approach to smoothing, not moving average smoothing as done by LOESS and other techniques

## Slide 102: We will penalize functions that are very wiggly
LOESS: Locally Estimated Scatterplot Smoothing
This is the “penalized regression” approach to smoothing, not moving average smoothing as done by LOESS and other techniques

## Slide 103: We will penalize functions that are very wiggly
LOESS: Locally Estimated Scatterplot Smoothing
This is the “penalized regression” approach to smoothing, not moving average smoothing as done by LOESS and other techniques
Zero for straight lines
Controls how “bad” wiggle is

## Slide 104: is the primary means to control fit quality

## Slide 105: can be chosen via cross-validation or restricted maximum likelihood (REML)
Generalized Cross-Validation (GCV)
Restricted Maximum Likelihood (REML)
Leave out an observation Estimate model Compute error on left-out observation Pick minimizing total error
Tends to pick smaller
Obtain a likelihood for
Pick maximizing the likelihood
Tends to pick larger

## Slide 106: can be chosen via cross-validation or restricted maximum likelihood (REML)
Generalized Cross-Validation (GCV)
Restricted Maximum Likelihood (REML)
Leave out an observation Estimate model Compute error on left-out observation Pick minimizing total error
Tends to pick smaller
Obtain a likelihood for
Pick maximizing the likelihood
Tends to pick larger

## Slide 107: Additive models permit lots of functional forms
Smooth main effects only

## Slide 108: Additive models permit lots of functional forms
Interaction surface

## Slide 109: Additive models permit lots of functional forms
Fully saturated smooth

## Slide 110: Additive models permit lots of functional forms
Decomposed* main effects
* We are not talking about the identifiability constraints today.

## Slide 111: Additive models permit lots of functional forms
Fully linear model

## Slide 112: Additive models permit lots of functional forms
And many more!

## Slide 113: GAMs can be extended to other situations
Shape-constrained additive models (SCAMs) incorporate smoothing functions that cannot take an arbitrary shape and need to satisfy some condition, such as being an increasing function (Pya and Wood 2015).
Additive quantile models estimate conditional percentiles of the response variable (Koenker 2011).
Functional additive models (FAMs) allow the factors or even the M&S outputs to be a function rather than a single number or label. For example, such a model could use as a predictor not only whether a missile hit or missed, or its miss distance; but also the missile’s entire flight path, or it could even predict what the typical flight path will look like based on input factors (Yao and Müller 2008).
Additive models and GAMs can model both location and dispersion, rather than location only. These models allow output variation to depend on the factors rather than be constant over the operational space.
Multiclass additive models determine the probability that an outcome is one of a number of potential outcome classes (Zhang et al. 2019).
GAM: Generalized Additive Model; M&S: Modeling and Simulation

## Slide 114: Model metrics can also reveal fit quality
Mean Square Error (MSE)
Minimized by average output
Influenced by outlier errors
Training set value: 3.1 m2
Evaluation set value: 3.8 m2
Mean Absolute Error (MAE)
Minimized by median output
Insensitive to outlier errors
Training set value: 1.4 m
Evaluation set value: 1.5 m
Maximum Error (MxE)
Worst-case-scenario error
Exclusively the error of outliers
Training set value: 6.7 m
Evaluation set value: 6.8 m

## Slide 115: Model metrics can also reveal fit quality
Mean Square Error (MSE)
Minimized by average output
Influenced by outlier errors
Training set value: 3.1 m2
Evaluation set value: 3.8 m2
Mean Absolute Error (MAE)
Minimized by median output
Insensitive to outlier errors
Training set value: 1.4 m
Evaluation set value: 1.5 m
Maximum Error (MxE)
Worst-case-scenario error
Exclusively the error of outliers
Training set value: 6.7 m
Evaluation set value: 6.8 m
No significant degradation between training and evaluation value; no evidence of overfitting

## Slide 116: We will analyze loop existence next (binary response)
Simulation outputs are now random; surfaces are irregular
The inputs are now the average rather than what was actually thrown due to “throw error”
How will we estimate the expected range, expected bumps, and probability of a loop?
WRPA: World Record Paper Airplane

## Slide 117: Before metamodeling, compute basic summary statistics
Design | Loop Probability | Sample Size
Dart | 0.40 | 100
Classic | 0.25 | 100
WRPA | 0.48 | 100
WRPA: World Record Paper Airplane

## Slide 118: We need to pick the functional form of the GAM
Description | Functional Form
Smooth Main Effects | 
Smooth Interaction | 
Plane-Design-Specific Smooth Terms | 
Smooth Saturated | 
Fully Linear Main Effects | 
Description | Functional Form
Smooth Main Effects | 
Smooth Interaction | 
Plane-Design-Specific Smooth Terms | 
Smooth Saturated | 
Fully Linear Main Effects | 
GAM: Generalized Additive Model

## Slide 119: We need to pick the response distribution and link function
* The canonical link function
Name | Description
Binomial | The usual binomial distribution
Quasibinomial | Allows for overdispersion (more variance than innate to the binomial distribution)
Name | Formula
Logistic* | 
Complementary Log-Log (CLL) | 
Probit | 
Name | Formula
Logistic* | 
Complementary Log-Log (CLL) | 
Probit | 
Distribution
Link Function

## Slide 120: We have additional metrics for assessing binary predictions
Brier Score
Accuracy
Proportion of correct predictions
Squared prediction error
Precision
How frequently a class was correctly predicted
Recall
How frequently predictions were correct

## Slide 121: These metrics may encourage overfitting
Brier Score
Accuracy
Proportion of correct predictions
Squared prediction error
Precision
How frequently a class was correctly predicted
Recall
How frequently predictions were correct
None of these metrics degrade in the training sample if we add irrelevant factors (that is bad)

## Slide 122: The Bayesian information criterion (BIC) can appropriately penalize complex metamodels
Brier Score
Accuracy
Proportion of correct predictions
Squared prediction error
Precision
How frequently a class was correctly predicted
Recall
How frequently predictions were correct
BIC
Rewards fit but punishes complexity

## Slide 123: We will use the screening set to help pick a metamodel based on OOS performance
TRAINING
SCREENING
EVALUATION
For estimating a metamodel
For seeing OOS performance and guiding metamodel choice
For computing final performance metrics
Used constantly
Used infrequently for helping choose between metamodel candidates
Used once, at the end
OOS: Out of Sample
We used training outputs to fit the metamodel
We use the screening set to help pick metamodels

## Slide 124: We narrow our selection down to three candidate metamodels (best BIC, best Brier score, and best accuracy)
BIC: Bayesian Information Criterion; CLL: Complementary Log-Log; OOS: Out of Sample
Formula | Distribution | Link | BIC | OOS Brier | OOS Accuracy | OOS Recall (No Loop) | OOS Recall (Loop) | OOS Precision (No Loop) | OOS Precision (Loop)
Smooth Main Effects | Binomial | Logit | 163.516 | 0.063 | 0.92 | 0.97 | 0.86 | 0.90 | 0.95
Smooth Main Effects | Binomial | Probit | 171.206 | 0.061 | 0.90 | 0.95 | 0.83 | 0.88 | 0.93
Smooth Main Effects | Binomial | CLL | 148.437 | 0.067 | 0.90 | 0.97 | 0.81 | 0.87 | 0.95

## Slide 125: Only the link function is in dispute
Formula | Distribution | Link | BIC | OOS Brier | OOS Accuracy | OOS Recall (No Loop) | OOS Recall (Loop) | OOS Precision (No Loop) | OOS Precision (Loop)
Smooth Main Effects | Binomial | Logit | 163.516 | 0.063 | 0.92 | 0.97 | 0.86 | 0.90 | 0.95
Smooth Main Effects | Binomial | Probit | 171.206 | 0.061 | 0.90 | 0.95 | 0.83 | 0.88 | 0.93
Smooth Main Effects | Binomial | CLL | 148.437 | 0.067 | 0.90 | 0.97 | 0.81 | 0.87 | 0.95
BIC: Bayesian Information Criterion; CLL: Complementary Log-Log; OOS: Out of Sample

## Slide 126: Cross-validation (CV) can also reveal OOS performance and imply its distribution
OOS: Out of Sample
Demonstration: 5-fold CV (5-CV)

## Slide 127: Cross-validation (CV) can also reveal OOS performance and imply its distribution
OOS: Out of Sample
Demonstration: 5-fold CV (5-CV)
Train metamodel
OOS

## Slide 128: Cross-validation (CV) can also reveal OOS performance and imply its distribution
Demonstration: 5-fold CV (5-CV)
Train metamodel
OOS
OOS: Out of Sample

## Slide 129: Cross-validation (CV) can also reveal OOS performance and imply its distribution
Demonstration: 5-fold CV (5-CV)
Train metamodel
OOS
OOS: Out of Sample

## Slide 130: Cross-validation (CV) can also reveal OOS performance and imply its distribution
Demonstration: 5-fold CV (5-CV)
Train metamodel
OOS
OOS: Out of Sample

## Slide 131: Cross-validation (CV) can also reveal OOS performance and imply its distribution
Demonstration: 5-fold CV (5-CV)
Train metamodel
OOS
OOS: Out of Sample

## Slide 132: Cross-validation (CV) can also reveal OOS performance and imply its distribution
Demonstration: 5-fold CV (5-CV)
We now have a distribution of OOS performance scores
OOS: Out of Sample

## Slide 133: We can use CV to visualize OOS performance and make a metamodeling strategy decision
The metrics vary widely among the link functions considered; our choice likely makes little difference to resulting fit quality
BIC: Bayesian Information Criterion; CV: Cross-Validation; OOS: Out of sample

## Slide 134: We will choose CLL link since it minimizes the BIC
BIC: Bayesian Information Criterion
CLL: Complementary Log-Log
OOS: Out of Sample
Formula | Distribution | Link | BIC | OOS Brier | OOS Accuracy | OOS Recall (No Loop) | OOS Recall (Loop) | OOS Precision (No Loop) | OOS Precision (Loop)
Smooth Main Effects | Binomial | Logit | 163.516 | 0.063 | 0.92 | 0.97 | 0.86 | 0.90 | 0.95
Smooth Main Effects | Binomial | Probit | 171.206 | 0.061 | 0.90 | 0.95 | 0.83 | 0.88 | 0.93
Smooth Main Effects | Binomial | CLL | 148.437 | 0.067 | 0.90 | 0.97 | 0.81 | 0.87 | 0.95

## Slide 135: Plotting the effect functions suggests improvements

## Slide 136: Plotting the effect functions suggests improvements
Huge smoothness penalty; this is basically a line, so replace smooth function with a linear effect

## Slide 137: Plotting the effect functions suggests improvements

## Slide 138: We can plot prediction regions of the metamodel
WRPA: World Record Paper Airplane

## Slide 139: We can construct a calibration plot to compare predicted probabilities versus observed outcomes
Conclusion: Do not reject ; insufficient evidence of metamodel miscalibration in training set

## Slide 140: A GAM struggled to construct a smooth relationship in the screening set
Conclusion: Reject ; evidence of metamodel miscalibration in screening set
???
GAM: Generalized Additive Model

## Slide 141: Metrics computed in evaluation set imply added predictive value and low evidence of overfitting
Brier Score
Accuracy
Proportion of correct predictions
Screen. set value: 0.9
Eval. set value: 0.89
Squared prediction error
Screen. set value: 0.067
Eval. set value: 0.11
Precision
How frequently a class was correctly predicted
Screen. set value (no loop): 0.87
Eval. set value (no loop): 0.89
Screen. set value (loop): 0.95
Eval. set value (loop): 0.88
Recall
How frequently predictions were correct
Screen. set value (no loop): 0.97
Eval. set value (no loop): 0.92
Screen. set value (loop): 0.81
Eval. set value (loop): 0.83
Design | Loop Probability | Sample Size
Dart | 0.40 | 100
Classic | 0.25 | 100
WRPA | 0.48 | 100
WRPA: World Record Paper Airplane

## Slide 142: Metrics computed in evaluation set imply added predictive value and low evidence of overfitting
Brier Score
Accuracy
Proportion of correct predictions
Screen. set value: 0.9
Eval. set value: 0.89
Squared prediction error
Screen. set value: 0.067
Eval. set value: 0.11
Precision
How frequently a class was correctly predicted
Screen. set value (no loop): 0.87
Eval. set value (no loop): 0.89
Screen. set value (loop): 0.95
Eval. set value (loop): 0.88
Recall
How frequently predictions were correct
Screen. set value (no loop): 0.97
Eval. set value (no loop): 0.92
Screen. set value (loop): 0.81
Eval. set value (loop): 0.83
Design | Loop Probability | Sample Size
Dart | 0.40 | 100
Classic | 0.25 | 100
WRPA | 0.48 | 100
The metrics are better than if we predicted the most common outcome based on plane design
WRPA: World Record Paper Airplane

## Slide 143: The calibration plot for the evaluation set looks fine
Conclusion: Do not reject ; insufficient evidence of metamodel miscalibration in evaluation set

## Slide 144: The calibration plot for the evaluation set looks fine
.x
Conclusion: Do not reject ; insufficient evidence of metamodel miscalibration in evaluation set

## Slide 145: The M&S Handbook contains a number of methods for validating M&S models…
M&S: Modeling and Simulation

## Slide 146: … we have seen another tool for doing VV&A…
VV&A: Verification, Validation, and Accreditation

## Slide 147: … and metamodeling provides more tools for both test planning and VV&A
VV&A: Verification, Validation, and Accreditation

## Slide 148: Two-sample tests ask if the distance between M&S typical behavior and behavior seen in live test data is large enough to discredit an M&S environment
DATA:
THRESHOLD:
In this illustration, the distance between the live and simulation mean estimates exceeds the threshold distance; reject
M&S: Modeling and Simulation

## Slide 149: Two-sample tests ask if the distance between M&S typical behavior and behavior seen in output is large enough to discredit an M&S environment
DATA:
THRESHOLD:
M&S: Modeling and Simulation

## Slide 150: Two-sample tests ask if the distance between M&S typical behavior and behavior seen in output is large enough to discredit an M&S environment
DATA:
THRESHOLD:
M&S: Modeling and Simulation

## Slide 151: Two-sample tests ask if the distance between M&S typical behavior and behavior seen in output is large enough to discredit an M&S environment
DATA:
THRESHOLD:
Should these be
Regression model coefficients?
Response functions (e.g. GAM smooth)?
Average response at select factor combinations?
GAM: Generalized Additive Model; M&S: Modeling and Simulation